## Slide 1: Hydraulic and Breach Analysis of a Dam in North Texas
Trina Muenzer
CE 394K.3
GIS in Water Resources
November 21, 2013

## Slide 2: Why is this important?
TCEQ regulates Dam Safety through Texas Administrative Code Ch. 299
Hydrology – safe passage of the probable maximum flood (PMF)
Hydraulics - Breach Analysis
  Safety of people and property downstream
  Emergency Action Planning

## Slide 3: Hydrology
72-hr PMF
Area ≤ 200 mi2
Chart: Time (Hours)
| 0 | 1.98 | 6
6 Hour | 0 | 13.2 | 22
12 Hour | 0 | 18.585 | 26.55
24 Hour | 0 | 24.96 | 31.2
48 Hour | 0 | 29.75 | 35
72 Hour | 0 | 32.725 | 38.5
HMR-51
Distribution
Notes: HYDROMETEOROLOGICAL REPORT NO. 51

## Slide 4: Hydraulics
Dam Characteristics
  Height, Length
  Spillway Dimensions
  Elevation, Storage, & Discharge Data
Stream Characteristics
  Cross-Sections

## Slide 5: A Dam in North Texas
Upper Dam:
  67 feet tall
  2,500 feet long
  Top of Dam = 934.7 ft-msl
  Spillway = 96-inch concrete pipe
  at 920 ft-msl
Lower Dam:
  80 feet tall
  1,750 feet long
  Top of Dam = 944.8 ft-msl
  Spillway = 72-inch concrete pipe
  at 920 ft-msl
Total Max. Storage = 102,250 ac-ft
Notes: Upper Dam was built in 1955 – point to original principal and emergency spillways
Lower Dam was built in 1980 – added boat pass, new emergency spillway
When the Lower Dam is at the top of dam, the two reservoirs become one….causing problems for modeling!!

## Slide 7: HEC-HMS Modeling
Notes: ADD MODEL RESULTS after fixing the model to run!

## Slide 8: HMS Results
Chart: Hours
| 1 | 2 | 3 | 6 | 12 | 24 | 48 | 72
Water Level | 930.3 | 934.8 | 934.8 | 934.9 | 935.8 | 938.7 | 939.4 | 940
Top of Dam | 944.8 | 944.8 | 944.8 | 944.8 | 944.8 | 944.8 | 944.8 | 944.8
Top of Dam (944.8 ft msl)
Water Level

## Slide 9
Elevation Data
  – converted to a TIN
River traced from NHD
Cross-sections added
Data exported to HEC-RAS
Notes: TIN - Triangulated Irregular network…..
Problems encountered – converting to a TIN takes up a lot of memory, make the DEM as small as possible before converting!
- use topography map or TIN to draw cross-sections, make sure cross sections aren’t too wide.

## Slide 10: HEC-RAS Results

## Slide 12
19.5 ft
30 ft
18 ft
31 ft

## Slide 13: Remaining Work
Modify HEC-HMS model
Sunny Day Breach
PMF Breach
Extend river cross sections

## Slide 14: Questions?