## Slide 1: GISWR: Témez Model
Application with GIS
Antonio Cañamás Catalá

## Slide 2: Objectives
Research the different GIS Databases for Spain
Apply Témez Model in a
Discuss whether the model is representative of the behavior of the Watersheds
Possible applications of the model: streamflow prediction with different scenarios; pumping, climate change…
Spanish Watershed
U.S. Watershed

## Slide 3: Témez Model
Rainfall-Runoff Model: uses Mass Balance
Data necessary:
Monthly Time Series for the last 25-30 years P, Streamflow, PET
Variables of the model to
approximate the behavior:
c, Hmax, Imax, α
Linear Reservoir Model

## Slide 4: Location of the Watersheds
Surface = 1396 km2
Surface = 921.16 km2

## Slide 5: Data Sources
Amount of evapotranspiration that would occur if enough water was available.
Thornthwaite Formula:
L  mean daylight hours of the month
N  no. of days in the month
Ti  mean monthly temperature
I  parameter that depends on Ti
α parameter that depends on I
Variable | Spain | U.S.
P |  | LDAStools
Streamflow |  | 
PET | No direct source | No direct source

## Slide 7: RESULTS
Spanish Watershed
U.S. Watershed

## Slide 8
Spanish Watershed
Bad approx. to peaks
Chart: Calibration
Calibration minimize the difference between observed and calculated

## Slide 9
Spanish Watershed
Chart: Validation
Starting to work accurately
More data needed!!!
Chart: Monthly mean values
| October | November | December | January | February | March | April | May | June | July | August | September
Calculated Streamflow | 13.4883 | 19.2101 | 10.2609 | 9.974 | 8.7678 | 6.9026 | 7.1451 | 12.3279 | 13.6258 | 8.9713 | 5.9887 | 7.898
Streamflow data | 11.5363 | 17.4324 | 9.4702 | 9.6561 | 8.7026 | 6.4278 | 6.5695 | 11.4986 | 13.8174 | 8.9962 | 5.8708 | 8.0986
November is a month with often peak flows
Biggest difference!!!

## Slide 10
U.S Watershed
Chart: Calibration
Bad approx. to peaks
Flood July 2002

## Slide 11
Chart: Monthly mean values
| January | February | March | April | May | June | July | August | September | October | November | December
Calculated Streamflow | 8.3224 | 12.308 | 16.0645 | 12.4775 | 24.6805 | 24.2868 | 14.6829 | 6.983 | 8.3265 | 11.6556 | 10.1009 | 9.8802
Data Streamflow | 10.6313 | 12.4148 | 15.8897 | 11.7965 | 13.4335 | 22.8306 | 16.8819 | 5.5168 | 5.7252 | 10.2079 | 14.6682 | 12.8645
U.S Watershed
Good approx. to base flows
Chart: Validation
| 39448 | 39479 | 39508 | 39539 | 39569 | 39600 | 39630 | 39661 | 39692 | 39722 | 39753 | 39783 | 39814 | 39845 | 39873 | 39904 | 39934 | 39965 | 39995 | 40026 | 40057 | 40087 | 40118 | 40148 | 40179 | 40210 | 40238 | 40269 | 40299 | 40330 | 40360 | 40391 | 40422 | 40452 | 40483 | 40513 | 40544 | 40575 | 40603 | 40634 | 40664 | 40695 | 40725 | 40756 | 40787 | 40817 | 40848 | 40878 | 40909 | 40940 | 40969 | 41000 | 41030 | 41061 | 41091 | 41122 | 41153 | 41183 | 41214 | 41244
Calculated Streamflow | 7.1716 | 7.079 | 7.501 | 6.918 | 6.8149 | 6.7268 | 6.7119 | 7.1666 | 6.4782 | 6.3946 | 6.312 | 6.2304 | 6.15 | 6.0705 | 6.1508 | 7.287 | 5.8576 | 5.7819 | 5.7072 | 5.6335 | 13.799 | 31.0207 | 9.0822 | 6.3465 | 25.9128 | 28.4451 | 31.5677 | 17.4224 | 30.9851 | 16.1096 | 16.946 | 6.3815 | 47.1701 | 6.5661 | 6.4813 | 6.3976 | 6.3299 | 6.2336 | 6.1531 | 6.0736 | 5.9952 | 5.9177 | 5.8413 | 5.7659 | 5.6914 | 5.6179 | 5.5453 | 6.296 | 7.2536 | 6.762 | 20.3982 | 5.4067 | 30.9539 | 5.5284 | 7.2643 | 5.3959 | 13.7302 | 5.3539 | 5.2847 | 5.2165
Data Streamflow | 4.4293 | 3.6444 | 3.7543 | 2.8625 | 2.0326 | 1.3358 | 1.3424 | 1.6231 | 0.9982 | 0.88737 | 0.91013 | 1.0315 | 1.0466 | 0.9111 | 1.2211 | 1.2991 | 1.2514 | 0.68039 | 0.46796 | 0.42093 | 3.2955 | 12.1654 | 11.3692 | 9.5184 | 23.4433 | 44.2057 | 19.7194 | 11.9711 | 11.5738 | 7.6113 | 7.8119 | 4.1942 | 20.4191 | 7.1748 | 5.402 | 4.6265 | 4.3079 | 3.1854 | 2.829 | 1.9597 | 1.4941 | 0.96884 | 0.81153 | 0.67804 | 0.66938 | 1.0391 | 0.91013 | 1.9568 | 5.4759 | 7.6177 | 14.5924 | 7.4058 | 12.5218 | 4.6534 | 3.1854 | 1.532 | 3.1194 | 2.7911 | 1.6147 | 1.4562
Trying to figure out why these big differences in some months
May….

## Slide 12: REMAINING TASKS

## Slide 13
Discuss the results for the U.S Watershed
Run a
        Climate change or Pumping simulation or both
        and analyze the results…
Reduce in P
and
Increase in PET
Aquifer Recharge - Pumping
(a period of time)

## Slide 14: Acknowledgements
Gonzalo Espinoza
Dr. David Maidment

## Slide 15
Questions?