## Slide 1: NZ’s Digital River Network
Dr Amy Whitehead
NIWA Christchurch

## Slide 2: NZ’s Digital River Network
Dendritic stream network
  > 576,000 individual reaches
  425,000 km of river
What is it?
Notes: 425 million km of river

## Slide 3: NZ’s Digital River Network
78 | 72 | 69 | 71 | 58
74 | 67 | 56 | 49 | 46
69 | 53 | 44 | 38 | 37
69 | 58 | 55 | 22 | 31
68 | 61 | 47 | 21 | 16
Digital elevation model
Stream network
Flow direction
How was it made?
Watersheds & catchments

## Slide 4: NZ’s Digital River Network
30m digital elevation model
Calculated local and upstream variables for each reach
  Elevation
  Slope
  Rainfall
  Geology
  Landcover
How was it made?
https://www.niwa.co.nz/freshwater-and-estuaries/management-tools/river-environment-classification-0

## Slide 5: NZ’s Digital River Network
Hydrological modelling
Water quality modelling
Classifying river environments
Predicting national river values
What is it used for?
TopNet

## Slide 6: NZ’s Digital River Network
Hydrological modelling
Water quality modelling
Classifying river environments
Predicting national river values
What is it used for?
CLUES
TopNet
Notes: Catchment landuse for environmental sustainability

## Slide 7: NZ’s Digital River Network
Hydrological modelling
Water quality modelling
Classifying river environments
Predicting national river values
What is it used for?
TopNet
CLUES
REC

## Slide 8: NZ’s Digital River Network
Hydrological modelling
Water quality modelling
Classifying river environments
Predicting national river values
What is it used for?
TopNet
CLUES
NZ River Maps
REC

## Slide 9: River Environment Classification (REC)
Hierarchical system for classifying river environments
  based on factors that control spatial patterns
Snelder, T.H., Biggs, B.J.F., 2002. J. Am. Water Resour. Assoc. 38, 1225–1239.
What is it?

## Slide 10: River Environment Classification (REC)
What is it?
Snelder, T.H., Biggs, B.J.F., Weatherhead, M., 2004. REC User Guide.
High Gradient
Medium Gradient
Low Gradient
Glacial
Mountain
Hill
Lowland
Lake
Cool – Dry
Cool – Wet
Cool – Very Wet
Warm – Dry
Warm – Wet
Warm – Very Wet
Alluvium
Hard Sedimentary
Soft Sedimentary
Volcanic Basic
Volcanic Acidic
Plutonic
Notes: The REC hierarchy consists of six controlling factors (hereafter referred to as factors), which define the six hierarchical levels of the classification. The first four levels group parts of rivers according to similarities in the Climate, Topography, Geology and Land-Cover of their catchments. The fifth and sixth levels group parts of rivers according to similarities in attributes of the local section of the river network: Network-Position and Valley-Landform.

## Slide 11: River Environment Classification (REC)
What is it used for?
Defining management units
Setting water quality limits
No periphyton
Normal periphyton
growth
Rapid periphyton
growth
Climate
Source of Flow
(Geology)
Climate
Geology

## Slide 12: Predicting national river values
Rainfall
Altitude
% Pasture
Distance
to sea
Mud
Notes: Predictive models showing the existing state Predictions show regional patterns and shouldn’t be used to assess conditions at specific sites. 108 predictive layers identified so far

## Slide 13: Predicting national river values
Rainfall
Altitude
% Pasture
Distance
to sea
Mud
Notes: Predictive models showing the existing state Predictions show regional patterns and shouldn’t be used to assess conditions at specific sites. 108 predictive layers identified so far

## Slide 14: Predicting national river values
Rainfall
Altitude
% Pasture
Distance
to sea
Mud
Mud
Notes: Predictive models showing the existing state Predictions show regional patterns and shouldn’t be used to assess conditions at specific sites. 108 predictive layers identified so far

## Slide 15: Predicting national river values
Rainfall
Altitude
% Pasture
Distance
to sea
Mud
Mud
River width
Sediment
Fish habitat
Water quality
E. coli
Invertebrates
MCI
Torrentfish
Hydrology
Fre3
Cobble
Width at
MALF
Notes: Predictive models showing the existing state Predictions show regional patterns and shouldn’t be used to assess conditions at specific sites. 108 predictive layers identified so far

## Slide 16: Predicting national river values
Notes: Published in many papers and reports but no method for making these data available for people to visualise or interrogate (other than terrible figures).

## Slide 17: NZ River Maps
A web-based tool to visualise and quantify spatial data for fresh waters
Amy Whitehead
Doug Booker
https://shiny.niwa.co.nz/nzrivermaps/

## Slide 19: NZ’s Digital River Network
NZ’s digital river network is a dendritic stream network calculated from a DEM
GIS files available from NIWA’s website
The digital river network has been used for
  Hydrological modelling
  Water quality modelling
  Classifying river environments
  Predicting national river values
View national predictions on the digital river network using NZ River Maps
Take home messages
https://shiny.niwa.co.nz/nzrivermaps/
(Search for REC!)