## Slide 1
The University of Texas at Austin
US Geological Survey
KISTERS
ESRI
Quarterly
Review
TxDOT Project 0-7095-01
Flood Assessment System for TxDOT (FAST)
8 July 2026
Notes: Allison

## Slide 2
  TxDOT Project Management Committee (PMC)
Rose Marie Klee – Lead Advisor TxDOT DES - H&H Section Director
Matthew Heinze – Lead Advisor
TxDOT MNT – Maintenance Support Section Manager
Chris Henry
TxDOT MNT – Deputy Director
Jared Browder
TxDOT MNT – TxMAP Specialist
Omar DeLeon
TxDOT MNT/AUS – Acting Deputy District Engineer/Director of Maintenance
Mark Wallace
TxDOT AUS – Bridge Engineer
ChunHo Lee
TxDOT BRG – Geotechnical Engineer
Mauricio Moreno
TxDOT ITD – Information Security Architect
Allison Wood
TxDOT DES / Huitt-Zollars
Jadé Adediwura – Project Manager
TxDOT RTI – Research Project Manager
Notes: Allison

## Slide 3
  TxDOT Technical Project Management Team (TPMT)
Rose Marie Klee – Lead Advisor TxDOT DES - H&H Section Director
Allison Wood
TxDOT DES / H&H Engineer – Deputy PM
Notes: Allison

## Slide 4
  TxDOT Technical Stakeholders
Matthew Heinze – Lead Advisor
TxDOT MNT – Maintenance Support Section Manager
Chris Rizzo
TxDOT MNT – Field Support Services Branch Manager/ Deputy Emergency Management Coordinator
Jared Browder
TxDOT MNT – TxMAP Specialist
Mysti Tran
TxDOT ITD – IT Planning & Admin System Branch Manager
MJ Jackson
TxDOT ITD – Management Analyst
Jason Henderson
TxDOT ITD – GIS Systems Architect
Mauricio Moreno
TxDOT ITD – Information Security Architect
Aiko Neill
TxDOT ITD – IT Contract Management Branch Manager
Lisa Ramirez
TxDOT ITD – Contract Administrator
Alonzo Balderaz
TxDOT ITD – GIS Development & Maintenance Lead
Priscillo Campos
TxDOT ITD – Management Analyst
Notes: Allison

## Slide 5
  Project Advisory Committee
NOAA Weather Forecast Office
Jonathan Brazzell
Regional Hydrologist, Lake Charles Office
Katie Landry-Guyton
Regional Hydrologist, Houston/Galveston Office
State and Local Agencies
Jorge Urquidi
City of Austin, FEWS Team
Sam Marie Hermitte
TWDB, Water Science Conservations
Christina Bryant
City of Austin, FEWS Team
Peter Smith
former TxDOT Director TPP
TxDOT H&H Section
Ab Maamar-Tayeb
Davis Magenheimer
Edra Brashear
Sara Armendariz
+ TxDOT Project Management Committee
Zenia De Leon
Harrison Smith
Abtin Hamedani
Stephanie Castillo
NOAA National Weather Service
Jason Johnson
Hydrologist-in-Charge, West Gulf River
Forecast Center
Fernando Salas
National Water Center, Geo-Intelligence Division
US Army Corps of Engineers
Jeff Linder
HCFCD
Derek Giardino
National Water Center, Geo-Intelligence Division
Carson Pruitt
National Water Center, Geo-Intelligence Division
Brent Higginbotham
Chief, Water Resources, Ft. Worth District
Chris Wright
Williamson County
Notes: Allison

## Slide 6
FAST Layers
Gauges
Research
Task 2
Flood Map Services
Task 3
Flood Decision Support Gauges
Task 4
Flood Transportation Geodatabase
Task 5
Flood Data
Services
Task 6
Forecast Data Analytics
Flood Map
Development
Flood Map Delivery
Field Mapping
Flood Emergency
Response Exercises
Gauge Operation and Maintenance
Gauge Calibration
RQ30 Flood Decision Support Toolbox Sites
Velocity – Stage Height Interaction
Synthetic Rating Curves
Road Elevation Model
Stream Hydrography
Road Inundation
Span Bridges
Bridge Class Culverts
Low Water Crossings
Bridge Warnings
Flooded Road Inundation
Flood Impact Assessment
Data Assimilation Implementation
Transportation Flood Impact Simulation
Probability of Road Overtopping
Assimilation in Space and Time
Regional Error Assessment
  Project Deliverables
Project Management
Organization, Coordination,
Reporting, and Communication
Dr. David Maidment
Kristine Blickenstaff
Notes: Tim

## Slide 7
Conducted training exercise / AUS & HOU
  AUS – Waco, San Antonio, Bastrop, SOC, Austin, Kerrville, H&H
  HOU - Houston, Montgomery, Beaumont, Bryan, Yoakum
Complied feedback from AUS & HOU
Ft Worth (July 28th) scheduled
  Project Management Plan Update – Oct 2025 to June 2026
Flood Decision Support Gauges
Flood Map Services
Flood Transportation Geodatabase
Flood Data Services
Gauges
Forecast Data Analytics
Research
FAST Layers
Prepped FAST for training exercises
Created Landing Page
Refactored & optimize FAST
Recomputed all 25 Districts bridges by Oak Ridge
O&M of the 80 RQ-30 sites – routine field trips, run levels, and streamflow measurements​
Data management and analysis of incoming sensor data – assess new approach and tools to improve efficiencies of gage calibration​
Worked on installation of updated power-supply and secondary telemetry equipment at select sites
Completed assessment of RQ-30 sites to be added to the FDST and prepared the synthetic rating curve publication for submittal to the journal
Forecasting accuracy assessment initiated and ongoing for entire FAST domain (Texas-Gulf Coast region)
FAST rainfall-runoff model developed and tested across Texas Hill Country
Notes: Tim

## Slide 8
  FAST
Notes: Tim

## Slide 9
  What is FAST
A website and service that gives predicted warnings and real-time updates about flooding on the Texas transportation network.
“An emergency response tool that helps TxDOT proactively plan for and respond to flood threats.”
Notes: Tim

## Slide 10
https://bridges.txdot.kisters.cloud/
  Live Demo
Notes: Tim

## Slide 11
How do I
access FAST?
Notes: Tim

## Slide 12
Devices:
Note: TxDOT staff must not use mobile applications while driving. Always focus on the road and follow all state and agency safety regulations
Notes: Tim

## Slide 13
1
2
3
4
5
1
All columns are sortable
2
How long since flood information was updated
3
Count of bridge warnings and road warnings impacted by forecasted flooding
4
Type to search
5
Click to view given row’s map
Navigate the dashboard:
Notes: Tim

## Slide 14
Statewide
Map
Notes: Tim

## Slide 15
My district’s
map
Notes: Tim

## Slide 16
Map Options:
1
Flood layers with toggles
2
Flood forecast model information
c
Toggle menu ‘sidebar’ on/off
4
5
Basemap and
Overlay map options
6
3
Provide user
feedback
Disclaimer Pop up
Notes: Tim

## Slide 17
Model Info:
2
Flood forecast model information
Most current flood forecast provided by
National Weather Service
1
Last hour in that forecast
2
Time when this FAST webpage was loaded
or refreshed
3
How old the forecasted data are in this webpage
4
Notes: Tim

## Slide 18
Why are the forecasts old:
How old the forecasted data are in this webpage
4
The National Water Model forecasts run on supercomputers and need time to gather, process, and check huge amounts of weather and river data, so the forecast results are usually available about 2+ hours after the current time.
Notes: Tim

## Slide 19
Flood Inundation Warnings:
1
Maximum flooding
limits expected in
“forecast window”
Notes: Tim

## Slide 20
Most current flood forecast provided by National Weather Service
What are these warnings:
FAST warnings point out the highest river levels that could happen at each location in the next 18 hours. If a FAST warning shows up, it means that spot could see flooding during that forecast window.
The forecasts are updated every hour with a completely new 18 hour look ahead.
Last hour in that forecast
Forecast Window
Notes: Tim

## Slide 21
Road Warnings:
1
Select flooded road
line for pop-up
N Levita Rd
Notes: Tim

## Slide 22
Bridge Warnings:
1
Select bridge warning point to get pop-up
Click “View cross section plot” – open in a new browser tab
3
Move slider to animate forecast
c
Forecasted stage (water surface) each hour on bridge
4
2
Notes: Tim

## Slide 23
Base maps and overlays:
Base Map: OpenStreetMap
Base Map: Google Hybrid
Overlay: TxDOT On-System (Roads)
Overlay: NOAA Radar (Live)
Overlay: Bridges Checked
i.e. where forecasts are evaluated
c
Notes: Tim

## Slide 24
Providing
Feedback:
1
2
Populate form & submit
Select Feedback Button
Notes: Tim

## Slide 25
Sample Feedback:
The system automatically records the map area you’re viewing and the time you make your comment, so you don’t need to enter these details—but you can if you want. Adding your username isn’t required, but it’s encouraged.
“forecast at this important bridge is missing”
“flood inundation limits in this area seem too big”
“roadway geometry is off”
“I wish the system could do …”
“System failed to load / crashed”
“I love / hate this tool”
Types of Comments we are looking for:
Notes: Tim

## Slide 26
Providing
Feedback:
3
Opens Survey
Notes: Tim

## Slide 27
Sample
Survey:
Hit SUBMIT to complete survey and record your information
Purpose is to allow the user to log additional information about a flooding location and upload photos
Notes: Tim

## Slide 28
How accurate is this system:
The FAST system provides estimates of river and flood conditions, but it isn’t always exact. Its predictions are based on weather forecasts and other information, which can change, so actual river levels may end up higher or lower than the warning suggests.
The FAST forecast updates every hour, so warnings will change. A warning might appear one hour, disappear the next, and then come back later as the latest data changes.
Notes: Tim

## Slide 29
Limitations:
Forecasted road and bridge flooding results are subject to limitations. Issues may include:
  missing or misaligned roads, bridges, or streams
  (2) incomplete or outdated terrain data
  (3) simplified floodplain modeling assumptions
  (4) limited forecast range.
Forecasts may not capture backwater effects, local ponding, or flash flood timing. Results should be considered estimates and SHALL NOT be used as official guidance.
Notes: Tim

## Slide 30
  Training Exercises
Notes: USGS

## Slide 31
  FAST Training Exercises
AUS Exercise
June 2, 2026 / 9-12pm
Districts: Waco, San Antonio, Bastrop, SOC, Austin, Kerrville, H&H
Number of Participants: 28
Number of Feedback Surveys: 24
HOU Exercise
June 10, 2026 / 1-4pm
Districts: Houston, Montgomery, Beaumont, Bryan, Yoakum
Number of Participants: 21
Number of Feedback Surveys: 11
FTW Exercise
July 28, 2026 / 1-4pm
Districts: Ft Worth, Dallas, Wichita Falls, Waco, Paris
Notes: Harry

## Slide 32
  Feedback
Overall Likes:
Ease of use
State-wide situational awareness
Ability to predict impact on roads & bridges
Historical view
Overall Requests:
Separate On/Off System bridges & Roads
Improve delay in Forecast
Filtering
Street Names
Notification
Overall Dislikes
Delay in forecast
No ability to filter on/off system bridges & roads
Want TxDOT street types
Need better street labeling
Overall Improvement Ideas:
Include scour bridges
Symbology changes (no black)
Real-time forecast
Improved historical functionality
Accuracy
Customization
Feedback –Team will categorize all the feedback from the exercises. From there, will determine which ones are actionable and then seek guidance from TxDOT on prioritizing the actionable list.
Notes: Harry

## Slide 33
  FAST Application
Notes: USGS

## Slide 34
Map updates:
  Lookback of past 24 hours
  Simulation mode
  Embedded cross section plots
Separate deployments of FAST:
  Evaluation (Production)
  Development
  Training
New products:
  Time-Lagged Ensemble forecasts – min/mean inundation maps.
  Export functionality
  FAST Updates – Web Application

## Slide 35
  FAST Updates – Backend
Compute time-lagged ensembles
  Min / Mean / Max for the next 12 hours
Implement first set of low water crossings
Performance improvement:
  Separate Input / Compute / Output tasks
  Use scalable workers for FAST layer generation and dispatching
  Use FlatGeoBuf output format.
  Javascript-based interactive cross-section plotting
  Increased concurrency of different products and IO

## Slide 36
  Discussion
Notes: Allison

## Slide 37
  Gauges – USGS
Notes: USGS

## Slide 38
  USGS – RQ-30 Measurements
RQ-30 Measurements Updates
  As of June 2026, 338 ADCP Measurements have been completed at RQ-30 sites
  At least 45 sites have fully calibration-quality data, and most sits have multiple measurements

## Slide 39
  USGS – RQ-30 Measurements
New Year Ck at FM 1155 nr Chappell Hill, TX
6 hours
19 hours
Guadalupe Rv at Comfort, TX
Chart: Lead spike vs Stage
| 8.02 | 9.01 | 10.039999999999999 | 10.220000000000001 | 14.76 | 8.85 | 9
 | 5.73 | 6.21 | 17.21 | 9.19 | 34.87 | 6.99 | 10.99
8.02 | 5.73 | 50 min
9.01 | 6.21 | 25 min
10.04 | 17.21 | 190 min
10.22 | 9.19 | 65 min
14.76 | 34.87 | 105 min
8.85 | 6.99 | 
9 | 10.99 | 

## Slide 40
  USGS – Equipment Updates
RQ-30 Equipment Updates
  21 Sites updated with XLIINK
  16 Fully updated to Iridium transmission

## Slide 41
  USGS – K-Factor Calibration Tool
Automated RQ‑30 calibration workflow built and in testing
Single tool integrates cross sections, ratings, ADCP, and validation
New method derives stage‑varying k‑factors from one ADCP transect
Early results match commercial tools and look promising

## Slide 42
  USGS – Flood Decision Support Toolbox (FDST)
RQ-30 Sites in the FDST
All Sites have been evaluated
  42 Active
  3 Pending upload
  1 Pending review
  34 Currently Poor Fit

## Slide 43
  USGS – Synthetic Rating Curve
  Evaluation Complete
    Statewide HAND comparison
    12 Traditional USGS streamgage comparisons
    Engineered channels and sites with downstream controls are not suitable
    No spatial variability
  Currently completing USGS Peer Review

## Slide 44
  Transportation Geodatabase
Notes: USGS

## Slide 45
https://www.fhwa.dot.gov/bridge/pubs/hif22034.pdf
  Building a New Road and Bridge Line Model

## Slide 46
https://www.fhwa.dot.gov/bridge/pubs/hif22034.pdf
  Building a New Road and Bridge Line Model

## Slide 47
Road Grade Line (x,y,z)
  The End Result: A 3D “Road Grade Line”
  with Bridges Included for Texas

## Slide 48
https://cfim.ornl.gov/data/t/bxw/alpha10/
State-wide coverage
(first draft)
  Road and Bridge Datasets for TxDOT Districts

## Slide 49
A point every 3m along the road
  3D Road Grade Line for this Bridge

## Slide 50
  Bridge on SH 136 NB over the Canadian River, Amarillo District

## Slide 51
  Research
  Accuracy assessment
Matt Bartos
Assistant Professor
Harsha Venkataraman
Graduate student

## Slide 52
  Forecasting accuracy assessment
Forecasting skill was previously assessed for San Antonio and Guadalupe river basins (68 gages)
We have now extended that assessment to the Texas-Gulf Coast HUC2 region (606 gages)
Goal: Evaluate skill of discharge forecasts under Nudging, Kalman Filtering, time-lagged ensembles

## Slide 53
Example discharge timeseries under Open-Loop, Nudging, and Kalman Filter
Initial assessment focused on 5/2023
Example site on Guadalupe river
Kalman Filter
Nudging
No DA

## Slide 54
  Current accuracy metrics considered
Continuous ranked probability score
(For a discrete set of M ensemble members):
Mean absolute error
Forecast spread
‘Within bounds’ score
Fraction of time observation is less than the maximum forecast value

## Slide 55
  Results: absolute forecast error (CRPS)
Higher worse
Lower better
Skill improvement
Skill improvement
Nudging
Kalman Filter
Kalman Filter
Nudging
No DA

## Slide 56
  Results: fraction of time observation is within forecast bounds
Over all gages, the observation is within the forecast bounds about 80% of the time
KF-Corr Better
Nudging Better
Fraction of time forecast in bounds

## Slide 57
  Research
  Improved hydrologic modeling
Matt Bartos
Assistant Professor
Harsha Venkataraman
Graduate student

## Slide 58
NWM forecasts are the primary limiting factor for timeliness and accuracy of forecasts
NWM forecasts have an inherent 2-hour delay, which limits flash flooding predictions
Use of NWM infiltration/runoff model precludes the use of enhanced rainfall data products (e.g. TTU data) that could improve forecasts.
  Purpose-built hydrologic model for FAST
Motivation
Solution
Custom hydrologic model based on a continuous-time Green-Ampt scheme.

## Slide 59
What is the overall accuracy of the hydrologic model?
Green-Ampt hydrologic model for San Antonio / Guadalupe river basins forced with 10 years of AORC gridded rainfall data. POLARIS soil parameters used.
Generated runoff and baseflow were routed through Muskingum routing model
Resulting discharge compared against 10 years of stream gauge data at outlet of San Antonio river basin
  Hydrologic modeling skill assessment
USGS Gage 08188570

## Slide 60
2020
2021
2022
2023
USGS Gage 08188570
Hydrologic skill before calibration is comparable to NWM

## Slide 61
Discharge in stream network
with rainfall field overlay

## Slide 62
Gage vs. Model with AORC forcing
Gage vs. Model with provided forecast
Comparison with measured discharge
USGS Gage 08167200
Guadalupe River near Bergheim
(In upper Guadalupe river downstream of Kerrville)

## Slide 63
  Parallel Considerations
TxDOT Districts
Hill Country Flooding, July 2025
$78 million legislative investment in flood forecasting, data and sirens
Main impact on TxDOT: Austin, San Antonio and San Angelo Districts
Texas Institute for Hazard Risk and Readiness (TIHRR) formed at Schreiner University in Kerrville
Contains a Flood Data, Intelligence and Training Laboratory

## Slide 64: NWS Public Flood Services
  Parallel Considerations
Precipitation (past and future)
Streamflow (probability of overbank flow)
Inundation Mapping (current conditions, next 5 days)
River Forecast Center points (Action, Minor, Moderate, Major)
Flood warnings

## Slide 65
  FAST and the NWS Forecasting System
FAST/srf_18hour_max_inundation_extent
FAST/srf_18hour_max_road_flooding
FAST/srf_18hour_bridge_warnings_time_profile
Short Range Forecasts
(Maximum for 18 hours ahead)
Flows and Mapping from NOAA
Flows and Mapping from NOAA
Flows from NOAA, mapping from TxDOT

## Slide 66: NOAA FIMPact Services
  Parallel Considerations
Compares predicted and measured stage height at USGS gauges
These services require permission from NOAA to be accessed

## Slide 67
  Discussion
Notes: Allison

## Slide 68
  Closing Comments
Notes: Allison