## Slide 1
Hydrologic model
Visualization
Stream gage network
Modeled discharges
Discharge measurements
Inundation geometries
Bridge and roadway geometries
Web services
Roadway flood depth
forecasts
Discharge estimates
Emergency response
Data assimilation
Architecture for a flooded road information system

## Slide 2
Hydrologic model
Visualization
Stream gage network
Modeled discharges
Discharge measurements
Inundation geometries
Bridge and roadway geometries
Web services
Roadway flood depth
forecasts
Discharge estimates
Emergency response
Data assimilation
Part 1: Flood hydrology and data assimilation
Matt Bartos
UT Austin

## Slide 3
Hydrologic model
Visualization
Stream gage network
Modeled discharges
Discharge measurements
Inundation geometries
Bridge and roadway geometries
Web services
Roadway flood depth
forecasts
Discharge estimates
Emergency response
Data assimilation
Part 2: Flood hydraulics and web services
Andy Carter
UT Austin

## Slide 4
Hydrologic model
Visualization
Stream gage network
Modeled discharges
Discharge measurements
Inundation geometries
Bridge and roadway geometries
Web services
Roadway flood depth
forecasts
Discharge estimates
Emergency response
Data assimilation
Flood forecasting starts with a hydrologic model…

## Slide 5
Hydrologic model
Visualization
Stream gage network
Modeled discharges
Discharge measurements
Inundation geometries
Bridge and roadway geometries
Web services
Roadway flood depth
forecasts
Discharge estimates
Emergency response
Data assimilation
1. hydrologic model
Flood forecasting starts with a hydrologic model…

## Slide 6
What are the basic model components required to translate rainfall forecasts into streamflow forecasts?
What rainfall forcing data would you use?
What model(s) or equation(s) would you use for simulating infiltration and runoff dynamics?
What model(s) or equation(s) would you use for simulating discharge in the channel network?
Hydrologic modeling questions:

## Slide 7
A basic framework…

## Slide 8
Rainfall forcings
Infiltration / runoff modeling
Streamflow routing
Data assimilation
Discharge forecasts
Hydrologic model

## Slide 9
Rainfall forcings
Infiltration / runoff modeling
Streamflow routing
Data assimilation
Discharge forecasts
Hydrologic model

## Slide 10
Gridded rainfall forcings
Forecast products
Retrospective
High-resolution rapid refresh (HRRR): 3km hourly gridded rainfall with 3km radar data assimilated every 15 minutes. 18-hour forecast every hour. 48-hour forecast every 6 hours.
Rapid refresh (RAP): 13km hourly gridded rainfall with 13km radar data assimilated. 18-hour forecast every hour.
Multi-radar / multi-sensor (MRMS): Provides nowcasts by combining models with radar and surface/air observations. Resolution of 1km every 2 minutes.
Analysis of record for calibration (AORC): 1km hourly gridded rainfall derived from multiple data sources, including NEXRAD and GDAS.
HRRR
HRRR
RAP

## Slide 11
For the FAST system, 18-hour HRRR forecasts are sourced from the National Water Model

## Slide 12
For the FAST system, 18-hour HRRR forecasts are sourced from the National Water Model
(Longer-horizon forecasts are generally not accurate enough for real-time response)

## Slide 13
Do you need forecasts or just nowcasts?
If you need forecasts, how far into the future? (1 hr, 18 hr, 48 hr…?)
At what time scale must emergency response decisions be made?
Choosing rainfall data:

## Slide 14
Rainfall forcings
Infiltration / runoff modeling
Streamflow routing
Data assimilation
Discharge forecasts
Hydrologic model

## Slide 15
Infiltration and runoff models
Commonly-used models for flood forecasting:
SAC-SMA: Conceptual model used within NWS River Forecast Centers to produce forecasts of stream discharge and stage. Divides soil into multiple ‘buckets’ with tension and free water zones to emulate real-world runoff, baseflow, and evapotranspiration dynamics. Runoff is divided into 5 different components contributed by 5 layers. Represents runoff primarily through saturation-excess mechanisms (best suited for humid catchments).
CREST: Conceptual model developed by the University of Oklahoma and NASA. Amenable to remote sensing datasets. Also uses multiple buckets to represent soil dynamics, but does not explicitly represent tension and free water components. Uses a variable-infiltration capacity (VIC) curve to determine the portion of the watershed that is contributing to runoff (generally suited for saturation-excess runoff in humid catchments).
SAC-SMA model
CREST model

## Slide 16
For the FAST system, we use the WRF-Hydro modeling system as implemented in the National Water Model
Infiltration
Runoff
Ground-water

## Slide 17
Runoff outputs are available for the Continental US via the NOMADS NCEP HTTP service

## Slide 18
For arid regions in Central / West Texas, the FAST system is testing an infiltration-excess model based on Green-Ampt with soil recovery
2020
2021
2022
2023
Green-Ampt infiltration
2-layer water balance

## Slide 19
Are there existing calibrated models for your domain?
Is flooding primarily driven by infiltration-excess or saturation-excess runoff? (e.g. arid vs. humid)
What soil parameter data are available for your domain? (e.g. SSURGO, POLARIS, drilling logs)?
Choosing an infiltration and runoff model:

## Slide 20
Rainfall forcings
Infiltration / runoff modeling
Streamflow routing
Data assimilation
Discharge forecasts
Hydrologic model

## Slide 21
Forecasted runoff must be routed through the drainage network to generate discharge forecasts

## Slide 22
Stream network routing models
Commonly-used models for channel routing:
Muskingum: Linear, unidirectional routing model. Each channel is parameterized by a travel time (K) and attenuation factor (X) that define the transport of the wave.
Muskingum-Cunge: Nonlinear, unidirectional routing model. Allows travel time (K) and attenuation (X) to vary depending on the discharge and depth of water.
Kinematic wave: Nonlinear, unidirectional routing model. A simplification of the Saint-Venant equations for unsteady flow considering only frictional and gravitational forces.
Diffusive wave: Nonlinear, bidirectional routing model. A simplification of the Saint-Venant equations considering frictional, gravitational, and hydrostatic forces.

## Slide 23
For FAST, streamflow routing is based on the Muskingum model
Prism storage
Wedge storage
Governing equation for a single reach:
Outflow at next timestep
Inflow at next timestep
Inflow at previous timestep
Outflow at previous timestep
Lateral inflow
Two parameters:
Flood wave travel time in reach [s]
Wave attenuation (from 0 – 0.5)

## Slide 24
For a large system of reaches (NHD), we can express the Muskingum model in terms of a large matrix equation
Muskingum Method, all reaches (state-space form):
xt+Δt
xt
ut
A
B
+
=
State-space simulation
Muskingum Method, single reach:
Muskingum model is forced by runoff inputs from National Water Model

## Slide 25
The result is a fast model that simulates 18-hour discharge forecasts for all of Texas in less than 3 seconds

## Slide 26
FAST routing code available via GitHub

## Slide 27
Are backwater effects important or is it possible to use a unidirectional model?
Is it important to represent nonlinearities in wave behavior?
What is the size of your model domain and how quickly do you need the model to run?
Choosing a routing model:

## Slide 28
Rainfall forcings
Infiltration / runoff modeling
Streamflow routing
Data assimilation
Discharge forecasts
Hydrologic model

## Slide 29
Why do we need data assimilation?
If you were tasked with fusing gauge data into a model (assuming no prior knowledge) how would you do it?
Are there any potential issues with your proposed approach?
Data assimilation questions:

## Slide 30
Data assimilation (DA) combines sensor data with a dynamical model…
sensor
model
…to improve estimation and forecasting of system states (like depths and discharges)

## Slide 31
Why do we need data assimilation?

## Slide 32
short answer: modeled forecasts are not reliable

## Slide 33
real overtopping event in new year creek
390 km2

## Slide 34
real overtopping event in new year creek
USGS stream gage

## Slide 35
real overtopping event in new year creek
USGS stream gage
overtopping discharge
overtopping location

## Slide 36
real overtopping event in new year creek
USGS stream gage
overtopping discharge
overtopping location
NWM short-term forecast
(1-hr lead time)

## Slide 37
real overtopping event in new year creek
real overtopping occurred on 5/15 and 5/16…

## Slide 38
real overtopping event in new year creek
But NWM forecast misses the main peaks…

## Slide 39
real overtopping event in new year creek
…and introduces five different false alarms

## Slide 40
To correct this problem, we can fuse discharge data from sensors into the routing model…
Measured + modeled depths
Assimilated depth
…to ensure that estimated discharges are accurate at the start of each forecasting window

## Slide 41
National Water Model (NWM)
calculates 100,000 cfs at in river
Gauge reads 50,000 cfs
Oops… only 50,000 cfs will be in the NWM
downstream of the gauge
NWM uses a DA approach called
‘Nudging’…
…which effectively inserts discharge observations into the model

## Slide 42
Data assimilation approaches:
Variational data assimilation (3DVAR/4DVAR): Common in numerical weather prediction. Minimizes an objective function defined in terms of the difference between estimated and observed states. 3DVAR incorporates 3 spatial dimensions while 4DVAR incorporates a time dimension.
Kalman Filtering / Smoothing: Data assimilation method common in control theory and numerical weather prediction. Minimizes the mean squared error between observations and the estimated system states. Kalman Filtering estimates the current state based on past and present observations. Kalman Smoothing estimates current and past states based on past and present observations. Kalman Smoothing is equivalent to 4DVAR.
Nonlinear Filters: Various filtering approaches exist for nonlinear systems, including Extended Kalman Filtering (EKF), Ensemble Kalman Filtering (EnKF), and Particle Filtering (PF). Many of these approaches are based on ensembles of models (EnKF, PF).

## Slide 43
The FAST system applies an optimal DA approach for routing called Kalman Filtering
under the following assumptions:
The measurement noise is Gaussian with known covariance Wk
The process noise is Gaussian with known covariance Vk
The initial error covariance is known
minimizes the mean squared error between the true and estimated states at each model timestep

## Slide 44
1 gauge
11 gauges
In essence, Kalman Filter applies an optimal ‘correction’ to the runoff input at the start of each forecast window
(correction)
(open-loop model)

## Slide 45
(a)
(b)
NWM
KF (6h)
USGS sensor
NWM
KF (1h)
USGS sensor
Forecasts at 6-hour lead time
Forecasts at 1-hour lead time
Result:

## Slide 46
Kalman Filtering significantly improves discharge forecasts compared to nudging
(perfect score)

## Slide 47
Is your system linear or nonlinear?
Do you care primarily about forecasting or prediction at ungaged locations?
Is the error in your model primarily due to parameter uncertainty or forcing uncertainty?
Choosing a data assimilation approach:

## Slide 48
Jeil Oh
Graduate Student
Matt Bartos
Assistant Professor
For more info, see:
Oh, J. & Bartos, M. (2025). Flood early warning system with data assimilation enables site-level forecasting of bridge impacts. npj Natural Hazards, 2(1), 64. DOI: 10.1038/s44304-025-00116-0.