## Slide 1
Real-Time Flood Engineering
Workshop Presented by
David Maidment, Andy Carter, Matt Bartos
Center for Water and the Environment University of Texas at Austin
Kristine Blickenstaff, Jon Thomas, Jody Avant US Geological Survey
Presented to:
Texas Floodplain Management Association Technical Summit
San Antonio, Texas Friday 28 August, 2026
Acknowledgments: Colleagues and students at University of Texas at Austin, NOAA National Weather Service, Texas Division for Emergency Management, Texas Department of Transportation, ESRI, KISTERS,

## Slide 2: Schedule
8:00 Introduction of presenters and participants
8:15 Introduction to Real-Time Flood Engineering (David Maidment)
9:00 Flood Decision Support Gauges and Toolbox (Kristine Blickenstaff, Jon Thomas, Jody Avant)
9:45 Break
10:00 Flood Hydrology and Data Assimilation (Matt Bartos)
10:45 Flood Hydraulics and Building a Real-Time Forecasting System (Andy Carter)
11:45 Conclusions and Discussion
12 noon Workshop ends

## Slide 3: Flood Assessment System for TxDOT (FAST)
Forecast
Precipitation
Forecast
Flood
Inundation
Forecast
Streamflow
David
Maidment
Kristine Blickenstaff
Forecast
Road and
Bridge Impact
An ongoing research project ending in Jan 2027

## Slide 4: Flood Decision Support Gages and Toolbox
Jody Avant
Jon Thomas
Kristine Blickenstaff

## Slide 5: Real-time Flood Hydrology and Hydraulics (Matt Bartos and Andy Carter)
Hydrology
National Water Model
Rainfall &
Discharge
Estimates
Hydraulics
Inundation Geometries
Real-time Mapping
Combine
to Map

## Slide 6: Flood Catastrophe in the Texas Hill Country
A failure in flood communications
137 died, including many children
“How can we do better?”
Legislative Hearing in Kerrville on
31 July 2025

## Slide 7: Flood Engineering
Traditional Flood Engineering
Accurate
Engineer: “I worry if I am wrong”
Real-Time Flood Engineering
Accurate, reliable and timely
First responder: “I worry if I am late”
Terrible lesson of 4 July flood at Camp Mystic – the warning was late

## Slide 8
Flood Warning Systems
Timeliness
Accuracy
Timeliness
Accuracy
Timeliness
Accuracy
Timeliness
Accuracy
David Curtis

## Slide 9: Flood Engineering
Traditional flood engineering
Real-Time Flood Engineering
Image: City of Long Beach https://www.longbeach.gov/disasterpreparedness/disaster-preparedness/hazard-mitigation-plan/

## Slide 10: Two Kinds of Rainfall Inputs
Design Storms
Real-Time Storms

## Slide 11: Flood Inundation Mapping – two national systems in the US
FEMA’s National Flood Hazard Layer
Salado Creek, San Antonio, Texas
Wabash and White Rivers,
Illinois and Indiana,
23 August 2026
NOAA’s Real-Time Flood Inundation Mapping

## Slide 12: Flood Inundation Mapping (FIM) – two methodologies
Frequency FIMs
FIM Libraries

## Slide 13: National Flood Forecasting
National Water Center
Established in 2014 in Tuscaloosa, AL

## Slide 14
Operational by National Weather Service in August 2016
Fernando Salas

## Slide 15: National Water Model
Four model outputs for forecast discharge:
Assimilation (Current conditions)
Short Range Forecast (18 hours ahead)
Medium Range (10 days ahead)
Long Range Forecast (30 days ahead)
Water forecast like weather 24/7/365
Water flow forecasts on 5.2 million km
of streams and rivers in US
2016
Initial CONUS Water Model
2019
Includes Hawaii
Medium Range Forecast
2021
Includes Puerto Rico …
Improved performance
2023
Includes part of Alaska
Combines riverine and coastal
Future
Next Generation
Modeling Framework
Versions

## Slide 16: Evolving Water Prediction Capabilities
~3,600 NWPS Forecast Points
RFC CHPS Forecast Models
FIM provided for ~ 110,000 river miles
~2.7M NWM Forecast Points
National Water Model (NWM)
FIM provided for ~ 3.4 million river miles
Extended
Forecasts
RFC

## Slide 17
National Flood Inundation Mapping deployed on 21 September 2026

## Slide 19
  Observational Flood Mapping
“P2F was a huge hit with the teams, from around the country, that responded to the July 4th and 5th, 2025 flood event. They all saw the practical applications for the incident managers and simplistic entry for the responders.” Jeff Saunders, Director, Texas Task Force 1
https://pin2flood.tdem.texas.gov/
https://www.youtube.com/watch?v=iGNwjI4k4qM

## Slide 20: Single Sign-On access to Pin2Flood
https://pin2flood.tdem.texas.gov
Comments from Melissa Ruiz, TDEM

## Slide 21: Flood Response with Maps at the State Operations Center
University of Texas Center for Water and the Environment
Emergency Management Flood Project – Pin2Flood
National Water Center
Predictive Flood
Mapping
Observational
Flood Mapping
State Operations Center
Local EOC
First responders in field
State Operations Center

## Slide 22: Method for Determining Flood Inundation Mapping (FIM) Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Computed for continental US
at the University of Illinois
Credit: Yan Liu, Shaowen Wang, David Tarboton, Utah State Univ.
FIM 1 in 2016
FIM 100 in 2026
Notes: How do we answer the question of how many people are going to be impacted, especially if large areas of the state are not covered by LIDAR or National Flood Hazard Layer? The researchers developed a process called Height Above Nearest Drainage or HAND.

## Slide 23: HAND Method

## Slide 24: Calculating Synthetic Rating Curves

## Slide 25: Discharge to Stage Height to Inundation Map
Stage Height (ft)
Discharge (cfs)
Synthetic Rating Curve

## Slide 26: NOAA Flood Map Services

## Slide 27: NOAA Flood Map Services

## Slide 28: Part 2. Flood Map Services

## Slide 29: Flood Decision Support System for Williamson County
https://wilcomaps.wilco.org/vertigisstudio/web/?app=f9563f4ce02f4fdd8f7f84249b500ec9
Flood map services assembled by Frank Martin and George Strebel, Wilco GIS
Four Components:
NOAA Flood Map Services
Local reference data
Precipitation (past and future)
Local flood services (including SB3)

## Slide 30
NWM FIM
Hydrofabric - Streams
HUC8 = 12070205 in Williamson County

## Slide 31
NWM FIM
“back end” data
(per HUC-8)

## Slide 32
NWM FIM
Catchments

## Slide 33
NWM FIM
“Full Res” HAND

## Slide 34
NWM FIM
“Main Stem” HAND

## Slide 35
NWM FIM
“FIMpact” Items

## Slide 36
https://www.fhwa.dot.gov/bridge/pubs/hif22034.pdf
  Federal Highway Administration Bridge Design Manual

## Slide 37
https://www.fhwa.dot.gov/bridge/pubs/hif22034.pdf
  Building a Road and Bridge Line Model

## Slide 38
Road Grade Line (x,y,z)
  The End Result: A 3D “Road Grade Line”
  with Bridges Included for Texas

## Slide 39
https://cfim.ornl.gov/data/t/bxw/alpha10/
State-wide coverage
(first draft)
  Road and Bridge Datasets for TxDOT Districts

## Slide 40
A point every 3m along the road
  3D Road Grade Line for this Bridge

## Slide 41: Bridge on SH 136 NB over the Canadian River, TxDOT Amarillo District

## Slide 42: Flood Transportation Geodatabase for Texas Built over last 10 years with support from TxDOT, TDEM, TWDB and TxGIO These data are publicly available
Flood Inundation Maps
190,000 stream miles
OpenStreetMap roads
470,000 road miles
in (x,y,z) for first time
LIDAR in 25 TxDOT Districts
269 Maintenance Sections
Total area: 269,000 Sq. Mi.
Cross-section profiles for 13,000 span bridges over water
3m FATHOM DEM for Texas

## Slide 43: Exploring Roads Flooded During a 10% Annual Chance Storm in Bexar County
Trinity Shuler, Jordan Merson

## Slide 44: Results
Overlay SARA Flood Water Surface Elevation on raster Road Elevation Model
Notes: Max depth & location of overtopping after clip for overall & parallel areas
Total number of impacted road segments in BC for overall & parallel areas

## Slide 45
Mitigation of Flood Impact on Roads and Bridges
Texas General Land Office: Mitigation Reallocation Program
Call for Project Submissions: Fall of 2026
Contact: Shawn Strange cdr.reallocation@recovery.texas.gov
Webpage:
https://www.glo.texas.gov/disaster-recovery/mitigation

## Slide 46: Frequency-Based Flood Modeling in Texas
Base Level Engineering
Hurricane Harvey Recovery
> $100 million investment

## Slide 47
Texas RBFS Model Data and Results Mapping
Accessing RBFS Model Results Data at Scale using
Comments by Jacob Beatty
Senior H&H Engineer
Open Source, Non-Proprietary
Robust API for Boundary Conditions
Solves HEC-RAS Linux Limitations
HDF Results >> Direct to Dataframe
Automated Meshing and Stored Maps
Cloud Native Mapping Outputs
RBFS 100% Models via TDSI DQMT
Louisiana Watershed Initiative
Statewide Model Inventory
Key Features for Flood Forecasting Workflows

## Slide 48: Discussion for Intro Session
How can flood mitigation engineering interact with real-time flood engineering?
How do we convert our inventory of engineering-based flood modeling into stage-based flood inundation map libraries for Texas?
What are the limitations of the National Water Model and its FIM and how can these be overcome at the local level?
How does all this relate to SB3 and flood sirens?
….. your ideas and comments are welcome!