## Slide 1: Evaluation of Surface Velocimetry for Streamgaging
Jody Avant
U.S. Geological Survey
Texas Floodplain Management Association Fall Technical Summit
August 27, 2026

## Slide 2: Approximately 800 Traditional USGS Streamgages now Supplemented by 80 sites Evaluating Surface Velocity Radar Sensors
Notes: In Texas, the USGS operates 787 stream gages, 80 of which are part of this project.
Putting into perspective

## Slide 3
Traditional USGS Discharge Determination
Wading Measurement using Point Velocity Meter
Bridge Deployed Measurement using Acoustic Doppler Current Profiler
USGS Stage-Discharge Rating Curve
Measure and Record
Gage Height Time Series
Discharge Time Series from
Gage Height Data and Rating Curve
Notes: “ Hydrologic technicians are in a lot of ways ,like a maintenance division. “. We build, we maintain and upgrade gage equipment, and we anticipate impacts to our systems.
Measurements are plotted on a charge vs stage to determine a stage discharge relationship. It takes many measurements to determine this relationship . And it is forever changing based on channel conditions and seasonal changes.

## Slide 4
Stage-Discharge Rating Curve used at Tradition USGS Streamgages

## Slide 5
** Use of manufacturer names does not imply endorsement by USGS
Measurement of Water Elevation and Velocity using Surface Velocity Radar Sensor (Sommer RQ-30 Radar Gage **)
**

## Slide 6: Cross Section Surveying 08041940-Green Pond Gully at FM 365 nr Fannett, TX
Channel geometry in-line with the velocity sensor
Low chord
Bridge deck / road elevation
Sensor elevation
Notes: Remember q = v*a
This is the Area component

## Slide 7: Cross Section Verification 08111051-Carters Ck at FM 60 nr College Station
Main channel shows approximately 30% reduction in area at low flows following the application of riprap on the right bank.

## Slide 8
Procedure for Computing Discharge using Surface Velocity Sensor

## Slide 9: Typical Gage Installation

## Slide 10
Advantages of Acquiring Surface Velocity Data
Velocity wave prior to high rise event
Variable Backwater in streams
Tidally Influenced Applications
Real-Time Discharge Calculation

## Slide 11: Data Observations – Velocity
08164150 - W Navidad Rv at I-10 nr Schulenburg, TX
Date/time
Stage ( ft )

## Slide 12: Data Observations – Velocity
08164150 - W Navidad Rv at I-10 nr Schulenburg, TX
Date/time
Stage ( ft )

## Slide 13: Data Observations – Initial Velocity Wave
08111110 - New Year Ck at FM 1155 nr Chappell Hill, TX
6 hours
19 hours

## Slide 14: Tidally Influenced Site
08031020 – Cole Ck at I-10 nr Orange, TX
Stage
Velocity
Notes: As water level rises tidally, the velocity decreases and vice versa

## Slide 15: Variable Backwater Effect
08096580 – Tehuacana Ck at Hwy 6 nr Waco, TX
Brazos
River
Tehuacana
Creek
Notes: As water level rises tidally, the velocity decreases and vice versa

## Slide 16: Variable Backwater Effect - Continued
Discharge Stg/Q
Discharge by velocity
08096580 – Tehuacana Ck at Hwy 6 nr Waco, TX
Date/time
Discharge ( cfs )
Notes: As water level rises tidally, the velocity decreases and vice versa

## Slide 17
Targeted Calibration of Surface Velocity Sensor
Surface Velocity -> Mean Channel Velocity
08111110 – New Year Ck at FM 1155 nr Chappel Hill, TX
Discrete Discharge Measurements at Targeted Gage Heights used to define the “K-factor” Relation – Can mean Fewer Measurements than Traditional Stage-Q Rating

## Slide 18
More gages leads to denser network to assist decision makers
Where method works, comparable discharge computations for ingestion into water models
Availability of “new” parameter of velocity
Observations
Notes: Sufficient data – gauge height and discharge for comparison to the rq30 discharge computation.
Sensors maintain adequate calibration
Speak on Uncertainty.
Uncertainty in discharge and gauge-height time-series data are determined and provide a suitable means for comparison with traditional USGS methods. These comparisons will be the basis of determining whether the equipment and methods are TRL 9, thus, are appropriate for deployment at any TxDOT bridge location

## Slide 19: Flood Intelligence in Action:
How InFRM Turns Multi-Agency Science into Basin-Level Decisions
Friday August 28, 2026
TFMA Workshop
By Kristine Blickenstaff, PE
Jon Thomas

## Slide 20: InFRM
Interagency Flood Risk Management (InFRM) Team -
FEMA Region 6 - Sponsor
U.S. Army Corps of Engineers (USACE)
U.S. Geological Survey (USGS)
National Weather Service (NWS)

## Slide 21: Why InFRM?
Goals
  Integrate information and simplify access to data
  Increase accuracy and timeliness of information
  Provide high resolution information and forecasts
  Enrich stakeholder participation
Mitigate and “inform” flood risk as a team
Collaborating Nationally, Empowering Locally

## Slide 22: The Flood Decision Support Toolbox

## Slide 23: A Formula for Flood Preparedness
Hydraulic Model
High-Resolution Terrain
Real-Time Streamgage Data
Life-Saving Flood Scenario Planning

## Slide 24: Flood Decision Support Toolbox
  Scenario Planning
  Pre-positioned map libraries
  NWS Flood Categories
  Historical Flood viewing
  Critical infrastructure
  Damage Estimates
  Real-Time Event Response
  USGS Streamgaging
  NWS FIM mapping
  NWS Forecasts
  Weather Conditions
  Transportation Conditions
  Reservoir Conditions

## Slide 25: FDST Functionality

## Slide 26: FDST Functionality
Select anywhere in the map to view estimated water depth

## Slide 27: FDST Functionality
Linked NWS River Forecast
Setup WaterAlert
Historical Peaks

## Slide 28: FDST Functionality

## Slide 29: FDST Functionality

## Slide 30: FDST Functionality

## Slide 31: FDST Functionality

## Slide 32: FDST Functionality – Texas – TWDB Partnership
Reservoir Conditions
Critical Infrastructure
Road Conditions

## Slide 33: FDST Functionality – Texas
Click ‘Report’ to see more details on estimated building damages and estimated costs
Print Map function also summarizes building damage in Texas
NOTE: costs CANNOT be tied back to individual buildings

## Slide 34: FDST Functionality – Texas
Texas viewer shows TXDOT road conditions

## Slide 35: FDST Functionality – Texas
Reservoir status available through Water Data for Texas (% full and % flood height)

## Slide 36: FDST Functionality – Texas
Reservoir status available through Water Data for Texas (% full and % flood height)

## Slide 37: FDST Functionality – Texas

## Slide 38: FDST Functionality – New Jersey

## Slide 39: FDST Functionality – New Jersey

## Slide 40: FDST Functionality – New Jersey

## Slide 41: FDST Functionality – New Jersey

## Slide 42: National Weather Service - FIMs

## Slide 43: Uncertainty in Modeling
“All models are wrong, but some are useful”
Model Uncertainty
  Tier A/B
  Rating Curve RMSE
  Uncertainty in forecasts
  NWS FIMS
Most confidence at gage location
Highest uncertainty
Highest uncertainty
Tributary Inflow

## Slide 44: Kristine Blickenstaff, PE Jon Thomas
Integrated Hydrology + Data Science
USGS
kblickenstaff@usgs.gov
jvthomas@usgs.gov
InFRM.us
webapps.usgs.gov/infrm/fdst/