## Slide 1: Flood Assessment System for TxDOT (FAST)
Presented by Andy Carter and David Maidment
Center for Water and Environment University of Texas at Austin
To the TWDB Flood Organizing Group,
Flood Inundation Mapping Committee
7 November 2025
Andy Carter
Dr. David Maidment

## Slide 2
Disclaimer

## Slide 3
Hydraulics and Mapping
Hydrology
Roadway flood depth
forecasts
Visualization
Web services
Emergency response
Flood Assessment System for TxDOT (FAST)
National Water Model
Modeled
Discharges
Data
Assimilation
Stream Gage
Network
Discharge
Measurements
Discharge
Estimates
Inundation Geometries
Bridge and roadway geometries

## Slide 4
80 TxDOT gages with RQ-30 radar sensors
FLOG/FIM Subcommittee Meeting,
5 April 2024
FLOG/FIM Subcommittee Meeting,
10 January 2025
Data Assimilation to produce updated forecasts
Hydrology Presented in Previous FLOG/FIM Meetings

## Slide 5: Fitting in with the National Weather Service Forecasting
Flows and Mapping from NOAA
Medium Range Forecasts
(Maximum for 5 Days Ahead)
This is a research level system that is under evaluation at TxDOT
https://maps.water.noaa.gov/server/rest/services/nwm
nwm/mrf_gfs_5day_max_inundation_extent (FeatureServer)
nwm/mrf_gfs_5day_max_inundation_extent (MapServer)
nwm/mrf_nbm_5day_max_inundation_extent (FeatureServer)
nwm/mrf_nbm_5day_max_inundation_extent (MapServer)
rfc/rfc_based_5day_max_inundation_extent (FeatureServer)
rfc/rfc_based_5day_max_inundation_extent (MapServer)
Flows from NOAA, mapping from TxDOT
Short Range Forecasts
(Maximum for 18 hours ahead)
FAST/srf_18hour_max_inundation_extent
FAST/srf_18hour_max_road_flooding
FAST/srf_18hour_bridge_warnings_time_profile
Flows and Mapping from NOAA
Analysis and Assimilation Model
(Current Condition)
nwm/ana_inundation_extent (FeatureServer)
nwm/ana_inundation_extent (MapServer)

## Slide 6: Flood Transportation Geodatabase for Texas Built over last 10 years with support from TxDOT, TDEM, TWDB and TxGIO These data are publicly available
Flood Inundation Maps
190,000 stream miles
OpenStreetMap roads
470,000 road miles
in (x,y,z) for first time
LIDAR in 25 TxDOT Districts
269 Maintenance Sections
Total area: 269,000 Sq. Mi.
Cross-section profiles for 12,000 span bridges over water
3m FATHOM DEM for Texas

## Slide 7
A website and service that gives predicted warnings and real-time updates about flooding on the Texas transportation network.
“An emergency response tool that helps TxDOT proactively plan for and respond to flood threats.”
What is FAST:
What is FAST
Rose Marie Klee
Adding more gages
Improving flood predictions
Real-time flood mapping
Flooded road limits
Emergency management

## Slide 8
FAST Live Demo
Live Demo: FAST - Dashboard

## Slide 9
Historic Viewer (Demo)
Historic FAST Map
Historic FAST Map

## Slide 10
Forecast Window

## Slide 11
Model Information

## Slide 12
Forecast Age

## Slide 13
Forecast Accuracy

## Slide 14
Flood Transportation Database
Flood Inundation
Preparing FAST for Real-Time Flood Warnings
Relies on pre-processed static geospatial & tabular data
Pre-computation establishes links between forecasted hydrology and geospatial impacts
Key pre-processing steps:
  Generate flood inundation maps using terrain, streams, and thresholds
  Identify roads and bridges at risk of flooding
  Assign thresholds & metadata (road type, class, bridge elevation)

## Slide 15
Case Study Area

## Slide 16
Road Segment Lines
2.64 Million ‘Public’ Road Segments
s_road_segment_ln

## Slide 17
Road Segment Lines
s_road_segment_ln

## Slide 18
Road Elevation Model (DEM)

## Slide 19
Road Elevation Model (DEM)

## Slide 20
Streamlines
t_nextgen_to_nwm
NWM Reach: 5671577
Eight (8) hydraulic libraries
per this hydrologic reach (NWM: 5671577)
NWM: 5671577 (hydrologic)
FIM reach: 24820092 (hydraulic)

## Slide 21
Sample Hydrologic Forecast
Date: 2025-07-05
Time: 09:00 GMT
Time: 04:00 CDT
NWM: 5671577
NWM Reach: 5671577
NWM Reach: 5671577
Short-range forecast (18 hour)
Peak: 35,940 cfs
@ 9:00 AM CDT
= 13:00 UTC

## Slide 22
Flood Inundation Polygons
Hydraulic reference: 24820092
Hydrologic Reference: 5671577 (NWM)
Nearest floodplain: Q = 35,062 cfs
s_flood_inundation_ar
With FAST, over 7.1 Million flood inundation polygons
across Texas

## Slide 23
t_road_flood_trigger
Road Segment Lines
Road_id: 2546591
nextgen_id: 24820092
feature_id: 5671577
min_flood_flow: 33648

## Slide 24
Bridge Points
s_bridge_pnt
FAST is can forecast at ~13k
hydraulic bridge points

## Slide 25
Bridge Points
s_bridge_pnt
t_bridge_rating_curve

## Slide 26
Bridge Forecasts

## Slide 27
FAST Automated Workflow
FAST detects new hydrologic forecasts
SQL script executes spatial queries via PostgreSQL/PostGIS
Forecasted streamflows are compared to flood thresholds for each stream segment
Generated Dynamic Layers
- Flooded road lines
- Bridge warning points
- Updated flood inundation polygons

## Slide 28
FAST Database (static layers)

## Slide 29
FAST Backend Technology Stack
docker pull civileng127/fast-update:20250504
git@github.com:andycarter-pe/fast_realtime.git
Cronjob: */14 * * * * /usr/bin/docker run --rm -e DB_PASSWORD=‘xxxxxxx' -t civileng127/fast-update:20250504

## Slide 30
Data Agnostic Layers for Desktop GIS

## Slide 31
FAST Web Viewer (mobile and desktop)

## Slide 32: Kerr County has 677 National Water Model flowlines and catchments …
… this is dense enough for a county-wide forecasting system
Limitations of FAST
2 hour delay in getting NWM discharge forecast data
Using Height Above Nearest Drainage (HAND) rather than hydraulic engineering models
Notes: The river and stream network is broken into reaches, each of which has a unique identifying number, and is surrounded by a local catchment area. NOAA has a Weather and Climate Operational Supercomputer (WCOSS) which is used to forecast the nation’s weather. In one part of the WCOSS resides the National Water Model which calculates flow in all the individual stream reaches of Kerr County, and of the nation as a whole (about 2.7 million stream reaches in all). Several forecast water forecast models are run, one for current conditions, another for short range forecasts out to 18 hours ahead, a third for long-range forecasts 10 days ahead. The current condition and short range forecasts are updated hourly.

## Slide 33
Hydrology
Hydraulics and Mapping
Roadway flood depth
forecasts
Visualization
Web services
Emergency response
Forecasting for Flash Flooding
Stream Gage
Network
Discharge
Measurements
Discharge
Estimates
Inundation Geometries
Bridge and roadway geometries
Data assimilation
with hydrology
Start with Radar Rainfall

## Slide 34
TxDOT Research Project: 0-7095-01
Project Duration: February 2024 – January 2027
Sponsor: Research and Technology Implementation Division (RTI)
Created by: Center for Water and the Environment (CWE) & Center for Transportation Research (CTR)
University of Texas at Austin