## Slide 1
Flood Hazard and Readiness for the Texas Hill Country
Presented by
David R. Maidment
Center for Water and the Environment
University of Texas at Austin
Presented at:
FLOG Workshop Austin, Tx Monday 2 February 2026
Acknowledgments: Colleagues and students at University of Texas at Austin, NOAA National Weather Service, US Geological Survey, Texas Department of Transportation, ESRI, KISTERS, Schreiner University

## Slide 2: Kerr County has 677 flowlines and catchments …
… flow forecast every hour by the National Weather Service
Mean reach length = 1.6 miles
Notes: The river and stream network is broken into reaches, each of which has a unique identifying number, and is surrounded by a local catchment area. NOAA has a Weather and Climate Operational Supercomputer (WCOSS) which is used to forecast the nation’s weather. In one part of the WCOSS resides the National Water Model which calculates flow in all the individual stream reaches of Kerr County, and of the nation as a whole (about 2.7 million stream reaches in all). Several forecast water forecast models are run, one for current conditions, another for short range forecasts out to 18 hours ahead, a third for long-range forecasts 10 days ahead. The current condition and short range forecasts are updated hourly.

## Slide 3: Radar Gauge on Guadalupe River at Comfort, 4 July 2025
The flash flood sent a signal ahead of itself – “I am coming”
Velocity spike
Velocity spike
Peak Gauge Height
1 hour and 35 mins
Peak Gauge Height

## Slide 4
Hydraulics and Mapping
Roadway flood depth
forecasts
Road Flooding
Bridge Flooding
Inundation Geometries
Bridge and roadway geometries
Web map services
Cell phones and computers
Flood Assessment System for TxDOT (FAST) -- Flood Impact on Roads and Bridges
Hydrology
National Water Model
Forecast
Discharges
Data
Assimilation
Stream Gage
Network
Measured Discharges
Adjusted Forecast Discharge

## Slide 5: Incorporating Radar Rainfall Forecasting
Hydrology
Hydraulics and Mapping
Water on the Ground
Water in the Air

## Slide 6: Flood Response Geodatabase for Texas Built over last 10 years with support from TxDOT, TDEM, TWDB and TxGIO These data are publicly available
Flood Inundation Maps
190,000 stream miles
OpenStreetMap roads
470,000 road miles
in (x,y,z) for first time
LIDAR in 25 TxDOT Districts
269 Maintenance Sections
Total area: 269,000 Sq. Mi.
Cross-section profiles for 12,000 span bridges over water
3m FATHOM DEM for Texas

## Slide 7: GeoAI for Flooding
Jack Dangermond, President
Questions:
Will I be flooded?
How much time do I have?
Can I get out?

## Slide 8: GeoAI-based Vehicle Navigation during Flood Conditions
AI Query Box
Ingram
Kerrville
Normal route
Route with flooding

## Slide 9: Lessons Learned
NWS water forecasting on the river and stream network is already sufficiently dense in the Texas Hill Country
Measuring velocity and water level yields more useful intelligence than measuring water level alone, particularly during flash flood conditions
Using data assimilation to adjust NWS forecasts with real-time local measurements works quickly and results in higher forecast accuracy
Flood response geodatabase is already available to support Hill Country counties
Web map services are a valuable way of transmitting water forecast information to computers and cell phones
Multiple flood web map services can be combined and interpreted using GeoAI for Flooding
Technology alone is not enough. Education and training are also needed
TxDOT Districts