## Slide 1: SOIL MAP OF THE PECOS RIVER BASIN
SEDAT YALCINKAYA
NOVEMBER 24, 2009

## Slide 2: OBJECTIVES
Processing the digital soil maps to obtain the input soil data for hydrologic modeling.
Comparison of different digital soil data (FAO, NATSGO, STATSGO, SSURGO)

## Slide 3: DIGITAL SOILS DATA FOR HYDROLOGIC MODELLING
WEAP Model Structure (Soil Moisture Method)
Input Parameters

## Slide 4: STUDY AREA
WATERSHEDS (HUC_8) | AREA (KM2)
13040212 | 1048.17619
13060011 | 11350.60629
13070001 | 6454.582529
13070002 | 2039.366686
13070003 | 2913.223075
13070004 | 5074.004481
13070005 | 1831.660091
13070006 | 3833.113807
13070007 | 16414.37423
13070008 | 4962.616022
13070009 | 2505.34438
13070010 | 1997.452143
13070011 | 2828.999238
13070012 | 2573.636942
TOTAL BASIN AREA | 65827.15611

## Slide 5: DATA SOURCE FOR SOILS
FAO: http://www.fao.org/geonetwork/srv/en/metadata.show
STATSGO: http://datagateway.nrcs.usda.gov/
Available at US and state levels
SSURGO: http://soildatamart.nrcs.usda.gov/
          http://datagateway.nrcs.usda.gov/
Available at County level
Tabular data are not reader friendly. They must be imported in an MS Access database template.

## Slide 6: SPATIAL DATA

## Slide 7: RELATIONSHIP BETWEEN SPATIAL & TABULAR DATA
Mapunit
Component
Horizon
mukey
cokey

## Slide 8: ATTRIBUTES TABLE-STATSGO
3 polygons share the same mapunit (mukey 673265)
Mapunit s7304 has 10 components in different percentages
First component (cokey 673265:1022795) has 2 layers

## Slide 9: ATTRIBUTES TABLE-SSURGO
100 polygons represent one mapunit
This mapunit (mukey:364641) represents 2 components
 | SSURGO | STATSGO
POLYGON | 2294 | 12
MAP UNIT | 34 | 5
COMPONENT | 87 | 38

## Slide 10: RESULTS
FAO
1/5.000.000
NATSGO
1:7.500.000
(Under development)
STATSGO
1/250.000
SSURGO
1:12.000 to 1:31.680
Level of use
FAO
(Least detailed)
NATSGO
STATSGO
SSURGO
(Most detailed)
Detail level of information
FAO – UN,
Generalized Worldwide soil map
NRCS of USDA, just for US

## Slide 11: RESULTS
It might be good for my purpose to study with NATSGO, but it is still under development.
FAO is easy to use for my model. First, I need to know the contents of its attribute table. I am currently working on this.
STATSGO is also good for my model, however I need to spend a lot of time for calculation of average values.
SSURGO is definitely much more detailed than I need.

## Slide 12: QUESTIONS?