## Slide 1
Nitrogen (N): Budgets, Estimated Loads, and Measured Exports
Lisa Helper 2011
Special Thanks to:
Ahmad Tavakoy, Tim Whiteaker (CRWR), Rich Mueller(USDA NASS Research and Development Division), and Doug Rundle (NASS Texas Office)

## Slide 2: Motivation/Introduction Quickly

## Slide 3: Regional Nitrogen (N) Sources
Agriculture
  Forest leeching
  Animal decomposition
  Lightning
Atmospheric Deposition
  NOy
  NO3
  NO4
  NH3
  Inorganic N deposition
Natural
  Fertilizer
  Livestock
  Fixation in crop & pasture lands
Human Waste
  Excretion/sewage water
  Landfill leeching

## Slide 4: Creating Fertilizer Nitrogen Data Layer
Fertilizer Input at county level
(kg N county-1 year-1)

## Slide 5
Livestock Input at county level
(kg N county-1 year-1)
Animal (number based on Census of Agriculture 2007) | N excretion rates in waste production [kg N animal-1yr-1]
Beef Cattle | 58.51
Dairy Cattle | 121.00
Pigs & Hogs | 5.84
Sheep | 5.00
Goats | 5.00
Horses | 40.00
Chickens (broilers-layers) | 0.07-0.55
Turkeys | 0.39
Creating Livestock N
Data Layer
CE 394 GIS WR 2011
Lisa Helper
5
(Boyer et al. 2002)

## Slide 6: Fixation in Pastures and Cropland
USDA Cropland Data Layer Project (2008)
Certain crops and plants “fix” their own Nitrogen – result is additional inputs of N from specific plants
Using CLD, area of these lands are assessed and quantified for N input

## Slide 7: Export Estimates
Test region:
  San Antonio
  Guadalupe
Two Methods
  RAPID
    (David et al. 2011)
  Processing with Schematic Network
    (Johnson 2009)

## Slide 8
Raw NHDPlus data
NHDplus has many catchments
and rivers
Ahmad Tavakoly developed a way to downscale these catchments and rivers using the thinner code attribute provided in NHDplus data
Thinnercode = 1

## Slide 9: County to Catchment Level
Livestock and
Fertilizer Inputs
(kg N km-1 year-1)
Density of Livestock
and Fertilizer N Inputs
(kg N yr-1/ km2)

## Slide 10: Density to Catchment Level
Identity function in Arc Toolbox's Analysis Overlay tools  developed joined attributes from counties and catchments
Summary Statistics
to get total N density per
catchment in attributes
  Multiply N density by
  catchment area
CE 394 GIS WR 2011
Lisa Helper
10

## Slide 11: Result: Inputs at Catchment Level
Livestock and Fertilizer N
Inputs for each up-scaled
catchment
(kg N yr-1)

## Slide 12: Modeling Nutrients
Nutrients?
RAPID
Schematic Network
(From Dr. Tim Whiteaker’s Lecture)
Atmospheric Model or Dataset
Vector River Network - High-Performance Computing River Network Model
Land Surface Model
A = cross sectional area = hydrolysis rate of organic N
= ammonia oxidation rate = cross sectional avg of
t = time (days) organic N concentration
Will divide N attribute by 365 to get time series
Nonpoint Sources
Decay

## Slide 13: Land Use vs. Inputs
Urban/developed
Urban/developed
Less Urban
Less Urban
How large of an effect does Land Use Land Cover (LULC) have on N inputs?

## Slide 14: How Much is Input from Agriculture for Both Basins?
Chart: 2007 San Antonio and Guadalupe NH4 Estimated Agriculture Inputs
San Antonio N load(kg total) | 19635286.8587
Guadalupe N load(kg total) | 82165162.9046
Urban/developed
Less Urban

## Slide 15: N Input Estimates vs. Measured Output
Measured Data from James McClelland’s Group at University of Texas Marine Science Institute.
Chart: 2007 San Antonio and Guadalupe NH4 Estimated Agriculture Inputs
San Antonio N load(kg total) | 19635286.8587
Guadalupe N load(kg total) | 82165162.9046
Chart: 2009 San Antonio and Guadalupe NH4 Measured Output
2009 San Antonio NH4 Output (mg/l) | 1.9813
2009 Guadalupe NH4 Output (mg/l) | 2.0369
Urban/developed
Less Urban
Urban/developed
Less Urban

## Slide 16: Summary
Collected and Compiled all Agriculture nitrogen non-point sources
Reduced the number of catchments and stream segments by using dissolve function and Fortran-based script
Reduced N inputs from county to catchment level
Use RAPID to model Nutrient flow from catchment to stream to the Gulf of Mexico
Develop and use Schematic Network tool in ArcGIS to model nutrient flow to the Gulf of Mexico
Compare with observations of NH4 fluxes and note LULC types
Future Work

## Slide 17: References
Boyer, E. W., C. L. Goodale, N. A. Jaworski, and R. W. Howarth. 2002. Anthropogenic nitrogen sources and relationships to riverine nitrogen export in the northeastern USA. Biogeochemistry, 57/58: 137-169.
David, Cédric H., David R. Maidment, Guo-Yue Niu, Zong-Liang Yang, Florence Habets and Victor Eijkhout. 2011. River network routing on the NHDPlus dataset. Journal of Hydrometeorology, 12(5): 913-934.
Han, H. J. and J. D. Allan. 2008. Estimation of nitrogen inputs to catchments: comparison of methods and consequences for riverine export prediction. Biogeochemistry, 91(2-3): 177-199.
Howarth, R.W., G. Billen, D. P. Swaney, A. Townsend, N. Jaworski, K. Lajtha, J. A. Downing, R. Elmgren, N. Caraco, T. Jordan, F. Berendse, J. Freney, V. Kudeyarov, P. Murdoch, Zhu Zhao-liang. 1996. Riverine Inputs of Nitrogen to the North Atlantic Ocean: Fluxes and Human Influences. Biogeochemistry, 35:75-139.
Johnson, Stephanie. 2009. “A general method for modeling coastal water pollutant loadings.” Dissertation, University of Texas at Austin: Civil, Architectural, and Environmental Engineering. UT Digital Repository: http://hdl.handle.net/2152/10654, 2011.
Whiteaker, Tim. “Schematic Processor”. PowerPoint presentation. Center for Research in Water Resources, Austin, TX 18 October 2011.
CE 394 GIS WR 2011

## Slide 18: Thank you Questions?
Lisa Helper

## Slide 19: Flow vs. Output
Chart: 2008-2009 San Antonio and Guadalupe NH4 Output Measurements
2008 San Antonio NH4 Output(mg/l) | 1.8996
2008 Guadalupe NH4 Output (mg/l) | 0.68919
2009 San Antonio NH4 Output (mg/l) | 1.9813
2009 Guadalupe NH4 Output (mg/l) | 2.0369
Chart: Guadalupe Basin Discharge (cfs) Measurements
| Time
Discharge (cfs) 2008 | 1370 | 1130 | 890 | 1190 | 757 | 591 | 576 | 573 | 643 | 562 | 522 | 556 | 1050 | 870 | 500 | 636 | 547 | 559 | 395 | 423 | 382 | 436
Discharge (cfs) 2009 | 464 | 476 | 395 | 428 | 295 | 4170 | 458 | 288 | 139 | 198 | 149 | 146 | 156 | 1350 | 1200 | 11900 | 15200 | 16700 | 11100 | 1870 | 1220 | 8510 | 25900 | 5930
Chart: San Antonio Basin Discharge (cfs) Measurements
| Time
Discharge (cfs) 2008 | 647 | 1150 | 1100 | 227 | 1840 | 910 | 422 | 262 | 282 | 291 | 281 | 289
Discharge (cfs) 2009 | 314 | 316 | 220 | 242 | 157 | 553 | 420 | 113 | 99 | 122 | 110 | 126 | 258 | 2030 | 1010 | 3060 | 6720 | 10400 | 8520 | 4010 | 1220 | 5170

## Slide 20
Fertilizer Input at county level
(kg N county-1 year-1)

## Slide 21
Livestock and Fertilizer Inputs
(kg N km-1 year-1)

## Slide 22: Getting the Nutrients to Catchment Level
Best Practice was to find Density of N within each county
Density of Livestock
and Fertilizer N Inputs
(kg N yr-1/ km2)

## Slide 23: What is Measured as Export?
Chart: 2008-2009 San Antonio and Guadalupe NH4 Output Measurements
2008 San Antonio NH4 Output(mg/l) | 1.8996
2008 Guadalupe NH4 Output (mg/l) | 0.68919
2009 San Antonio NH4 Output (mg/l) | 1.9813
2009 Guadalupe NH4 Output (mg/l) | 2.0369
(McClelland Data)