## Slide 1
Application of spatial autocorrelation analysis in determining optimal classification method and detecting land cover change from remotely sensed data
Edward Park
SAC in MATLAB
Digital Globe inc.

## Slide 2
Introduction
  1.1 Objective
Objective:
To do the accuracy assessment of various classification of raster pixels
Why?
The ultimate goal of Geographic Information System (GIS) is to model our world. However, the modeling process is too complicated and requires elaborateness that we should not rely entirely on computer.
  How?
Comparing with hand digitized reference image and look into how the error pattern varies depending on classification methods by using spatial autocorrelation analysis.
Spatial resolution issue

## Slide 3
Introduction
  1.2 Study Area
Lake Travis in Austin Texas, USGS EE
Cypress Creek Arm, Google Earth (approximately 2km*1.5km)

## Slide 4
Introduction
  1.3. Data Source
Scene
· 2009 Landsat 7 ETM+ Images from USGS
· LE70270392009032EDC00
· LE70270392009064EDC00
Reference data
· 2009 Aerial Photograph from Capcog (capcog.org) and Trinis (trinis.org)
· TOP0809_50cm_3097_33_4_CIR_01062008 (natural color)
· TOP0809_50cm_3097_33_4_NC_01062008 (color infrared)
· MANSFIELD_DAM (29 mrsid files stitched)
· Field Visit with GPS
· Other reference data
· Land-cover map, vegetation cover map, hydrograph map,
- Google earth (for oblique view), daily water level data of Lake Travis from 2009

## Slide 5
Introduction
  1.3. Data Source
  - Some Justification and Projection
Metadata from Landsat
Aerial Orthophoto taken around…early noon!! 3? 4?
VS

## Slide 6
Introduction
  1.3. Data Source
  - Some Justification and Projection
UTM Zone 14
Almost through the standard line!!
Lake Travis water level
Approximately same level between dates
(Feb. 1 & Feb. 3)
- From http://travis.uslakes.info/Level.asp

## Slide 7
2. Preprocessing
  - Overview
Three major analysis will be introduced in this research using spatial autocorrelation:
analysis of error produced based on different types of classification method
2) monthly change detection using spatial autocorrelation,
3) changing pattern of error depending on spatial resolution.

## Slide 8
2. Preprocessing
  - Overview, 2.1 Digitizing
Reclassify
Difference Image
Run Spatial Autocorrelation
Hand Digitize
Orthohphoto O
Orthohphoto X
MANSFIELD_DAM (29 mrsid files stitched)
from CAPCOG

## Slide 9
2. Method
  2.2 Preprocessing
Feature Space Plot
Spectral Reflectance Curve
Assign:
- Water to 1
- Tree to 2 - Grass to 3
- Urban to 4
Sand to 5
  Based on Spectral Value !!
Reference Map!!
Threshold 7.5 meter
Mosaic
Clip
Project
Digitize..etc

## Slide 10
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
10 methods of classifications were used !
Mostly Supervised (8):
One Unsupervised:
Parametric MLH (Maximum Likely Hood)
Parametric MHN (Mahalanobis)
Parametric MND (Minimum Distance)
Parallelepiped MLH
Parallelepiped MHN
Parallelepiped MND
Feature Space MLH
Feature Space MND
ISODATA (5 classes)
MLH (but used 30 signature produced by ISODATA process)
Will add PCA (Principal Component Analysis) in final project
Clip!!
Resampled (30 ->10m)

## Slide 11
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Supervised Classification
Training Sites Pickup in ERDAS
Imagine’s Signature Editor
Water
Tree
Grass
Urban
Sand
the trickiest!!

## Slide 12
TrainingSites_Separability
Plot of all training sites
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Supervised Classification

## Slide 13
Spectral Reflectance Curve
=
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Supervised Classification

## Slide 14
Classified Images!! (half way product)
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Supervised Classification

## Slide 15
(Reference Image)
(Classified Image)
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Creating Difference Image
-
-
(Difference Image)
=
* Ranges from -4~4, reclassified into 0~4

## Slide 16
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Difference Image

## Slide 17
One Unsupervised:
One Unsupervised:
2. Method
  2.2 Preprocessing of Image ‘to be’ classified
  - Difference Image
Final Product!! (ready to start analysis)

## Slide 18
Spatial Autocorrelation (SAC): 1st rule of geography,
“everything is related to everything else, but near things are more
related than distant things” – Waldo Tobler
2. Method
  2.2 Spatial Autocorrelation
– correlation of a variable with itself through space.
– If there is any systematic pattern in the spatial distribution of a variable, it is said to be spatially autocorrelated.
– If nearby or neighboring areas are more alike, this is positive spatial autocorrelation.
– Negative autocorrelation describes patterns in which neighboring areas are unlike.
– Random patterns exhibit no spatial autocorrelation.
A rule that makes geography so meaningful!!

## Slide 19
Moran’s I
General G
2. Method
  2.2 Spatial Autocorrelation
Global SAC
Local SAC
LISA
Xi is the variable value at a particular
Location, Xj is the variable value at another
Location, X is the mean of the variable
Wij is a weight applied to the comparison
between location i and location j

## Slide 20
Simplification of line when vectorizing
Conceptualization of Spatial Pattern
2. Method
  2.2 Spatial Autocorrelation
Again, some justifications

## Slide 21
3. Result
  3.1 Global SAC
Lowest!! (looks like computer won over me)

## Slide 22
3. Result
  3.2 Local SAC

## Slide 23
3. Result
  3.3 General G Statistics

## Slide 24
Spatial resolution issue
3. Conclusion and Limitations
There is spatial autocorrelation pattern of errors.

## Slide 25
Questions?
Suggestions?
◆ Visualization of results (including plotting rook’s, queen’s bishop’s cases)
- Further Plan
◆ Also perform initial statistical analysis based on number of pixels for each class
◆ Try to look for other classification method (Linear SMA, Fisher linear discriminant etc)
◆ Regression analysis (explanatory_var: reference image, dependent_var: classified image )