## Slide 1: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 2: Six Basic Course Elements
Lectures
  Powerpoint slides
  Video streaming
Readings
  Handouts and lecture synopses
Homework
  Computer exercises
  Hand exercises
Term Project
  Oral presentation
  PDF report
Class Interaction
  Email
  Discussion
Examinations
  Midterm, final

## Slide 3: Our Classroom
Dr David Tarboton
Students at Utah State University
Dr David Maidment Students at University of Texas at Austin
Dr Ayse Kilic Students at University of Nebraska - Lincoln

## Slide 4
B.E. in Agricultural Engineering (with First Class Honors) from University of Canterbury, Christchurch, New Zealand, 1972
MS, PhD in Civil Engineering from University of Illinois, 1974 and 1976, respectively
1981 – joined University of Texas at Austin as an Assistant Professor, and have been on the faculty ever since. Now Hussein M. Alharthy Centennial Chair in Civil Engineering
Initiated the GIS in Water Resources course in 1991 – this is the 21st birthday of this course!
Worked with ESRI since 1994 on a GIS Hydro Preconference seminar for the ESRI Users Conference
Leader of the CUAHSI Hydrologic Information System project from 2004-2011
Developing World Water Online with ESRI and Kisters
David R. Maidment

## Slide 5: David Tarboton
B.Sc Eng in Civil Engineering from the University of Natal, Durban, South Africa 1981
M.S. and Sc.D from MIT, Cambridge, Massachusetts, 1987 and 1990 respectively
1990 - Joined Faculty at Utah State University in Civil and Environmental Engineering
1996 - Developed D-Infinity to have a better contributing area for study of landscape evolution
Gradually adapted the Fortran and C codes developed during terrain analysis research to be distributable as TauDEM
Participated in GISWR since 1999 (this year is the 13th time)
Leader of HydroShare project to extend the capability of CUAHSI HIS to collaborative data sharing, additional data types and models

## Slide 6
M.E. (1998) & Ph.D (2002). Agricultural and Biological Engineering. University of Florida. Gainesville, FL. Dissertation: “Linking multiple layers of information to explain soybean yield variability” . 5 papers
2004- Joined to UNL and continued to work on computer simulation of crop production for another year and gradually moved to Remote Sensing field with applications in Natural Resources Systems.
2006 - Remote Sensing-based Estimation of Evapotranspiration and other Surface Energy Fluxes
Research innovations include the development of new soil heat flux algorithms, a spatially gridded distributed soil water balance model (DSWM), and calibration techniques for the Landsat-based METRIC evapotranspiration model.
2008- Working on development of the Nebraska Hydrologic Information System (HIS), which is designed to provide improved access to evapotranspiration and other hydrologic data for end users.
Participated in GISWR since 2006 (this year is the 5th time – I skipped 2007 due to position change at UNL)
Ayse Kilic

## Slide 7: University Without Walls
Traditional Classroom
Community
Inside and Outside
The Classroom

## Slide 8: Learning Styles
Instructor-Centered Presentation
Community-Centered Presentation
Student
Instructor
We learn from the instructors and each other

## Slide 9: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 10: What is GIS
A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present all types of geographical data. -- Wikipedia
maps
data
tools
computers

## Slide 11: Geography is visualized in maps
www.arcgis.com
map

## Slide 12: Maps are built from data
map
data
Road
Name: E. Dean Keeton St
Type: Div Highway
Speed: 35 mph
Shape: [Geometry]
Building
Name: Ernest Cockrell Jr Hall
Address: 301 E. Dean Keeton St
Shape: [Geometry]
Shape includes the geometry of the feature and where it is located on earth

## Slide 13: Vector data represent discrete features
map
data
polygons
lines
points

## Slide 14: Raster data form a grid of cells or pixels
map
data

## Slide 15: More Raster Examples
map
data
rainfall
elevation
land use

## Slide 16: There are many more data types
map
data
triangulated
irregular network
multipatch
annotation
Martin Luther King Dr W

## Slide 17: Connected Map, Chart and Animation
Hurricane Isaac
http://www.msnbc.msn.com/id/26295161/ns/weather/

## Slide 18: Geographic Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 19
Data Model based on Inventory of data layers

## Slide 20: Spatial Data: Vector format
Point - a pair of x and y coordinates
(x1,y1)
Line - a sequence of points
Polygon - a closed set of lines
Node
vertex
Vector data are defined spatially:
Notes: DRM

## Slide 21: Kissimmee watershed, Florida
Themes

## Slide 22: Attributes of a Selected Feature

## Slide 23: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 24
http://srtm.usgs.gov/srtmimagegallery/index.html
Santa Barbara, California

## Slide 25: The challenge of increasing Digital Elevation Model (DEM) resolution (Dr Tarboton’s research)
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 26: How do we combine these data?
Digital Elevation
Models
Watersheds
Streams
Waterbodies

## Slide 27: An integrated raster-vector database

## Slide 28: Remote Sensing Coverage of Nebraska
P33R30
10
P32R30
9
P31R30
10
P30R30
9
P29R30
10
P33R31
11
P32R31
10
P31R31
12
P30R31
9
P29R31
11
P28R31
8
P33R32
15
P32R32
8
P31R32
12
P30R32
10
P29R32
12
P28R32
10
P27R32
8

## Slide 29: Evaporation from Remote Sensing (Dr Kilic)

## Slide 30: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 31: Linking Geographic Information Systems and Water Resources
GIS
Water
Resources

## Slide 32: A Key Challenge
GIS
Water Environment
(Watersheds, streams, gages, sampling points)
How to connect water environment with water observations
Time Series Data
Water Observations
(Flow, water level concentration)

## Slide 33
CUAHSI is a consortium representing 125 US universities
Supported by the National Science Foundation Earth Science Division
Advances hydrologic science in nation’s universities
Includes a Hydrologic Information System project
http://www.cuahsi.org

## Slide 34: How the web works
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Catalog harvest
Search
HTML – web language for text and pictures

## Slide 35
Rainfall
Water quantity
Meteorology
Soil water
Groundwater
We Collect Lots of Water Data
Water quality

## Slide 36: The Data have a Common Structure
A point location in space
A series of values in time
Gaging – regular time series
Sampling – irregular time series
Notes: These data are recorded over time to monitor a hydrologic process or property.

## Slide 37: WaterML as a Web Language for Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P17D&parameterCd=00060
I accessed this WaterML service from USGS at 4:29PM
and got back these flow data from USGS which are up to 3:45PM
USGS has real-time WaterML services for about 11,000 sites available 24/7/365
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P1D&parameterCd=00060

## Slide 38
Hydrologic Information System
Analysis, Modeling,
Decision Making
Arc Hydro
Geodatabase
A synthesis of geospatial and temporal data supporting hydrologic analysis and modeling

## Slide 39: ArcGIS Online
GIS on the web – online map services
http://www.arcgis.com

## Slide 40: Online Base Maps (20 scales)

## Slide 41: Topographic Base Map in ArcGIS Online
World
United States
Texas
Austin
Home

## Slide 42: World Hydro Overlay Map
World
United States
Texas
My Home
My Stream

## Slide 43: GIS in Water Resources: Lecture 1
In-class and distance learning
Geospatial database of hydrologic features
GIS and HIS
Curved earth and a flat map

## Slide 44: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 45: Latitude and Longitude
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 46: Latitude and Longitude in North America
90 W
120 W
60 W
30 N
0 N
60 N
Austin:
Logan:
Lincoln:
(30°18' 22" N, 97°45' 3" W)
(41°44' 24" N, 111°50' 9" W)
(40°50' 59" N, 96°45' 0" W)

## Slide 47: Map Projection
Curved Earth
Geographic coordinates: f, l
(Latitude & Longitude)
Flat Map
Cartesian coordinates: x,y
(Easting & Northing)
Notes: DRM

## Slide 48: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 49: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin
Geographic Coordinates
Projected Coordinates

## Slide 50: Summary (1)
GIS in Water Resources is about empowerment through use of information technology – helping you to understand the world around you and to investigate problems of interest to you
This is an “open class” in every sense where we learn from one another as well as from the instructors

## Slide 51: Summary (2)
GIS offers a structured information model for working with geospatial data that describe the “water environment” (watersheds, streams, lakes, land use, ….)
Water resources also needs observations and modeling to describe “the water” (discharge, water quality, water level, precipitation)

## Slide 52: Summary (3)
A Hydrologic Information System depends on water web services and integrates spatial and temporal water resources data
Geography “brings things together” through georeferencing on the earth’s surface
Understanding geolocation on the earth and working with geospatial coordinate systems is fundamental to this field