## Slide 1: Data Sources for GIS in Water Resources by David R. Maidment, and David G. Tarboton GIS in Water Resources Fall 2013

## Slide 2: Learning Objectives
The hierarchical system of watersheds and basins
Where to obtain data and maps
  National/State/Global Data repositories
  Hydrography
  USGS National Water Information System
  Land Cover
  Elevation
  Soil (Statsgo/Surgo)
  Weather

## Slide 3: Water Resources Regions of the US
Region 01 New England Region 02 Mid-Atlantic Region 03 South Atlantic-Gulf Region 04 Great Lakes Region 05 Ohio Region 06 Tennessee Region 07 Upper Mississippi Region 08 Lower Mississippi Region 09 Souris-Red-Rainy Region 10 Missouri Region 11 Arkansas-White-Red Region 12 Texas-Gulf Region 13 Rio Grande Region 14 Upper Colorado Region 15 Lower Colorado Region 16 Great Basin Region 17 Pacific Northwest Region 18 California Region 19 Alaska (Old numbering system) Region 20 Hawaii Region 21 Caribbean
There are 18 water resources regions in the Continental United States
2-digit water resource regions

## Slide 4: Watershed Hierarchy
8 HUC
4
2
6
NHDPlus
10
12
Available
In Progress
Digit #
Each hydrologic unit is identified by a unique hydrologic unit code (HUC) consisting of two to eight digits based on the four levels of classification in the hydrologic unit system.

## Slide 5: Hydrologic Unit Code Watersheds
~ 2000 HUC 8 for US, about the size of counties

## Slide 6: Watershed Boundary Dataset
National Program by USGS and USDA (NRCS)
Boundaries for 10- and 12- digit watersheds
First cut is by automated delineation from NED
Hand checked and edited
10-digit watersheds
ftp://ftp.ftw.nrcs.usda.gov/wbd/WBD_Latest_Version_June2013/

## Slide 7
River networks
for 8-digit HUC
watersheds
http://nhd.usgs.gov/

## Slide 9: NHDPlus Reach Attributes
Slope
Elevation
Mean annual flow
  Corresponding velocity
Drainage area
% of upstream drainage area in different land uses
Stream order

## Slide 10: River Reach Codes Used for river address locations
ReachCode =
12030102000151
ReachCode = 12030102000005
HUC#
Segment#
Location 0.392
on Reach
12030102000005

## Slide 11: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m) cells
Seamless in 1° blocks for the United States
10 billion data
Derived from USGS 1:24,000 quadrangle sheets
Get the data:
http://ned.usgs.gov/
http://nationalmap.gov/viewer.html

## Slide 12
From hhttp://nationalmap.gov/viewer.html

## Slide 13
For LIDAR data: Go to http://lidar.cr.usgs.gov/

## Slide 14: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 15
Digital Elevation Model (DEM)-30 meter

## Slide 16: Austin West 30 Meter DEM

## Slide 17
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 18: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 19: Delineation of Streams and Watersheds on a DEM

## Slide 20
http://srtm.usgs.gov/

## Slide 21: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 23: GTOPO30 - 1 km Digital Elevation Model of the Earth
https://lta.cr.usgs.gov/GTOPO30

## Slide 24: Drainage in North America
Hydro1K is
derived from
GTOPO30
using raster
GIS analysis
https://lta.cr.usgs.gov/HYDRO1K

## Slide 25: Soil Data
http://websoilsurvey.nrcs.usda.gov/app/WebSoilSurvey.aspx
http://www.soils.usda.gov/survey/geography/ssurgo/
http://www.soils.usda.gov/survey/geography/ssurgo/description_statsgo2.html
Natural Resources Conservation Service (NRCS)
National Cartography and Geospatial Center (NCGC)
State Soil Geographic Database-STASGO
Soil Survey Geographic Database- SURGO

## Slide 26
1:250,000 Scale Soil Information

## Slide 28
http://websoilsurvey.sc.egov.usda.gov/DataAvailability/SoilDataAvailabilityMap.jpg
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps

## Slide 29: Ssurgo for Travis County
103 soil map units described by 7530 polygons of average area 35.37 ha (87 acres)

## Slide 30
http://landcover.usgs.gov/

## Slide 31: National Land Cover Dataset
Get the data:
http://www.mrlc.gov/
1992, 2001, and 2006

## Slide 33
http://www.nationalatlas.gov/atlasftp.html

## Slide 34
http://www.ncdc.noaa.gov/oa/ncdc.html

## Slide 35: PRISM Mean Annual Precipitation (Oregon State U.)
http://www.wcc.nrcs.usda.gov/climate/prism.html

## Slide 36: National Water Information System
Web access to USGS water
resources data in real time
http://waterdata.usgs.gov/usa/nwis/

## Slide 37: USGS Water Watch
Web access to USGS water resources data in real time
http://waterdata.usgs.gov/nwis/rt

## Slide 38: USGS National Water Information System.
Real-time and Historic Data
  Streamflow and stage
  Groundwater levels
  Water Quality
  Site information
Tabular or Graphical Format

## Slide 39: http://water.weather.gov/ahps/

## Slide 40: http://water.weather.gov/ahps/

## Slide 41
http://www.wcc.nrcs.usda.gov/snotel/

## Slide 42: http://www.cbrfc.noaa.gov

## Slide 43: CBRFC SNOTEL Ensemble
http://www.cbrfc.noaa.gov/station/sweplot/sweplot.cgi?tglu1

## Slide 44
Texas Natural Resource Information System http://www.tnris.org/

## Slide 45: TWDB http://www.twdb.state.tx.us/mapping/gisdata.asp

## Slide 46: http://gis.utah.gov

## Slide 47: Utah Terrain Basemap
To use as a basemap in ArcGIS see instructions at
http://gis.utah.gov/map-services/new-utah-terrain-base-map-and-cached-tile-service-available

## Slide 48
Utah GIS Portal Download GIS Data
http://gis.utah.gov/data/

## Slide 49
http://geology.utah.gov/maps/gis/index.htm

## Slide 50
http://www.wrcc.dri.edu/

## Slide 51: Bear River Watershed
http://www.bearriverinfo.org/

## Slide 52: Great Salt Lake Info System
http://greatsaltlakeinfo.org/

## Slide 53: What is Cloud Computing? Following Slides are from Dr Kristin Tolle, Microsoft Research Connections
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 54: Global Footprint
Where is the Cloud?
Notes: Speaking Points:
Windows Azure itself is deployed around the world
With Windows Azure, we have a concept of regions, which is where you choose to place your code and run.
In each of the regions, we have a Microsoft datacenter.
These datacenters are massive facilities that host 10s or in some cases hundreds of thousands of servers
We have currently four regions in North America, two regions in Europe, and two in Asia
As you can see on this slide we also have a number of CDN edge points, which we can use to cache your content and deliver it even faster for customers. %
What you’re going to see in the next couple months and years is that we will rapidly expand our datacenter footprint around the world, so you will have more options for running your applications.
Once you build an application, you can choose where you want to run in the world and you can move your workloads from region to region.
You can also run your application in multiple regions simultaneously and just direct traffic and customers to whichever version of the app is closest to them.
That gives you a global footprint and a chance to reach a bigger customer base or audience in new markets
Notes:
Windows Azure services such as compute and storage are now available in 8 worldwide datacenters with an additional 24 Content Delivery Network endpoints.
You can’t have a real cloud without a data center.

## Slide 55: Microsoft’s Data Center Evolution
  Chicago and Dublin Generation 3
  Data Center Co-Location Generation 1
  Modular Data Center Generation 4
  Quincy and San Antonio Generation 2
Time to Market
Lower TCO
Scalability & Sustainability
Rack
Density & Deployment
Server
Capacity
Containers
IT PAC
  Deployment Scale Unit
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 56
Inside a Container
Compute Rack
2 “Side by Side” Servers
Disk Sled Rack
Disk Sled Rack
On the truck
At the Manufacturer’s
Austin Plant (Dell)
Notes: Slide Objectives:
I want to demystify the cloud for the audience
Transition:
Transition statement(s) to setup the slide
Speaking Points:
These are containers built by the PC manufacturer at their Austin facility
Speaking Point #2
Notes:

## Slide 57: Containers arriving in Longmont Colorado
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 58: Modular Cloud Construction
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 59
Compute/Storage Container
Transformer & UPS
Air Flow Vents
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 60: Completed Cloud Computing facility in Longmont, Colorado
Notes: Slide Objectives:
Main points you want to make
Transition:
Transition statement(s) to setup the slide
Speaking Points:
Speaking Point #1
Speaking Point #2
Notes:

## Slide 61: ArcGIS Online: Maps about the Earth
http://www.arcgis.com/features/maps/earth.html
Land Cover
Soils
Elevation

## Slide 62: Landscape Grid Services

## Slide 63: Elevation Services

## Slide 64: Dynamic Map Services

## Slide 65: Extract the NHDPlus Flowlines

## Slide 66: Elevation Profile of the Blanco River
Chart: Blanco River Elevation Profile
Slope = 0.2%