## Slide 1: Terrain Analysis Using Digital Elevation Models
David Tarboton
Utah State University
dtarb@usu.edu
http://hydrology.usu.edu/taudem

## Slide 2: Outline
TauDEM software
D-Infinity flow model
Generalized flow accumulation (Flow algebra)
Parallel algorithms
Programming

## Slide 3: Topography defines watersheds which are fundamentally the most basic hydrologic landscape elements.
http://www.nap.edu/catalog/11829.html
www.hiwaysafety.com
Notes: Topography defines watersheds which are the most basic hydrologic landscape elements
Almost all hydrologic research requires information about "the watershed". Knowing what is in a watershed, what its attributes are, what is upstream and what is downstream are fundamental to understanding and protecting our water resources
FEMA and other federal and state agencies are spending millions on improved flood plain mapping based on DEMs

## Slide 4: Deriving Hydrologically Useful Information from Digital Elevation Models
Raw DEM
Pit Removal
Flow Field
Flow Related Terrain Information

## Slide 5: TauDEM Software
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables
http://hydrology.usu.edu/taudem/

## Slide 6: The starting point: A Grid Digital Elevation Model
Contours
720
700
680
740

## Slide 7: D8 Contributing Area

## Slide 8: Stream Reach and Watershed

## Slide 9: Edge contamination
Edge contamination arises when a contributing area value depends on grid cells outside of the domain. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 10: Outline
TauDEM software
D-Infinity flow model
Generalized flow accumulation (Flow algebra)
Parallel algorithms
Programming

## Slide 11: Representation of Flow Field
D
D8
67
56
52
48
Steepest single direction
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.)
Notes: This slide shows how the terrain flow field is represented. Early DEM work used a single flow direction model, D8. In 1997 I published the Dinfinity method that proportions flow from each grid cell among downslope neighbors. This, at the expense of some dispersion, allows a better approximation of flow across surfaces.

## Slide 12
D8
Contributing Area
D

## Slide 13: Wetness Index
Slope (S)
Specific Catchment Area (a)
Wetness Index ln(a/S)

## Slide 14: Terrain Stability Mapping
SINMAP - with Bob Pack. http://www.engineering.usu.edu/dtarb/sinmap.htm

## Slide 15: Most Likely Landslide Initiation Points
The location of the lowest Stability Index value along a flow path
Tarolli, P. and D. G. Tarboton, (2006), "A new method for determination of most likely landslide initiation points and the evaluation of digital terrain model scale in terrain stability mapping," Hydrol. Earth Syst. Sci., 10: 663-677, www.hydrol-earth-syst-sci.net/10/663/2006/.

## Slide 16: Most Likely Landslide Initiation Points compared to observed landslides
Tarolli, P. and D. G. Tarboton, (2006), "A new method for determination of most likely landslide initiation points and the evaluation of digital terrain model scale in terrain stability mapping," Hydrol. Earth Syst. Sci., 10: 663-677, www.hydrol-earth-syst-sci.net/10/663/2006/.

## Slide 17: Outline
TauDEM software
D-Infinity flow model
Generalized flow accumulation (Flow algebra)
Parallel algorithms
Programming

## Slide 18
Flow Accumulation
x
w(x)

## Slide 19: Generalization to Flow Algebra
Replace
by general function
Pki
Pki
Pki
i

## Slide 20
Useful for a tracking contaminant or compound subject to decay or attenuation

## Slide 21: Transport limited accumulation
Supply
Capacity
Transport
Deposition
Useful for modeling erosion and sediment delivery, the spatial dependence of sediment delivery ratio and contaminant that adheres to sediment
S
2
2
)
tan(
b
T
cap
ca
=
å
+
=
}
,
min{
cap
in
out
T
T
S
T
å
-
+
=
out
in
T
T
S
D

## Slide 22: Outline
TauDEM software
D-Infinity flow model
Generalized flow accumulation (Flow algebra)
Parallel algorithms
Programming

## Slide 23: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 24: TauDEM Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 25: TauDEM Parallel Approach
MPI, distributed memory paradigm
Row oriented slices
Each process includes one buffer row on either side
Each process does not change buffer row

## Slide 26: Parallelization of Flow Algebra
Executed by every process with grid flow field P, grid dependencies D initialized to 0 and an empty queue Q. FindDependencies(P,Q,D) for all i for all k neighbors of i if Pki>0 D(i)=D(i)+1 if D(i)=0 add i to Q next
Executed by every process with D and Q initialized from FindDependencies. FlowAlgebra(P,Q,D,,) while Q isn’t empty get i from Q i = FA(i, Pki, k, k) for each downslope neighbor n of i if Pin>0 D(n)=D(n)-1 if D(n)=0 add n to Q next n end while swap process buffers and repeat
1. Dependency grid
2. Flow algebra function

## Slide 27: Improved runtime efficiency
Parallel Pit Remove timing for NEDB test dataset (14849 x 27174 cells  1.6 GB).
128 processor cluster
16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
8 processor PC
Dual quad-core Xeon E5405 2.0GHz PC with 16GB RAM

## Slide 28: Scaling of run times to large grids
Chart: PitRemove run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 9.5315 | 529.3877 | 4817.6293
Total (OWL 8) | 12.0132 | 680.5546 | 6224.5029
Compute (VPC 4) | 1502.2881 | 4779.8761
Total (VPC 4) | 2120.0307 | 5695.2647
Compute (Rex 64) | 10.3477 | 139.9145 | 701.7363
Total (Rex 64) | 255.8499 | 3758.8385 | 24045.0594
Owl is an 8 core PC (Dual quad-core Xeon E5405 2.0GHz) with 16GB RAM
Rex is a 128 core cluster of 16 diskless Dell SC1435 compute nodes, each with 2.0GHz dual quad-core AMD Opteron 2350 processors with 8GB RAM
Virtual is a virtual PC resourced with 48 GB RAM and 4 Intel Xeon E5450 3 GHz processors
Chart: D8FlowDir run times
| 0.12000000000000002 | 2.14 | 4
Compute (OWL 8) | 355.6897 | 4363.094 | 10558.4924
Total (OWL 8) | 357.8926 | 4570.5555 | 11599.0188
Compute (VPC 4) | 10658.033 | 36568.8896
Total (VPC 4) | 11191.1583 | 37098.2448
Compute (Rex 64) | 198.0345 | 2854.9228
Total (Rex 64) | 429.8418 | 11384.6786

## Slide 29: Teton Conservation District, Wyoming LIDAR Example
Open Topography http://www.opentopography.org/

## Slide 30: DEM derived from point cloud using TIN DEM Generation and output as GeoTIFF

## Slide 31: Contributing area from D-Infinity
Notes: Note the detail in the representation of flow paths at features such as roads

## Slide 32: Contributing area from D-Infinity
Notes: Note the detail in the representation of flow paths at features such as roads

## Slide 33: Outline
TauDEM software
D-Infinity flow model
Generalized flow accumulation (Flow algebra)
Parallel algorithms
Programming

## Slide 34: Programming
C++ Command Line Executables that use MPI
ArcGIS Python Script Tools
Python validation code to provide file name defaults
Shared as ArcGIS Toolbox

## Slide 35: Q based block of code to evaluate any “flow algebra expression”
while(!que.empty())
{
//Takes next node with no contributing neighbors
temp = que.front(); que.pop();
i = temp.x; j = temp.y;
// FLOW ALGEBRA EXPRESSION EVALUATION
if(flowData->isInPartition(i,j)){
float areares=0.; // initialize the result
for(k=1; k<=8; k++) { // For each neighbor
in = i+d1[k]; jn = j+d2[k]; flowData->getData(in,jn, angle);
p = prop(angle, (k+4)%8);
if(p>0.){
if(areadinf->isNodata(in,jn))con=true;
else{
areares=areares+p*areadinf->getData(in,jn,tempFloat);
}
}
}
}
// Local inputs
areares=areares+dx;
if(con && contcheck==1)
areadinf->setToNodata(i,j);
else
areadinf->setData(i,j,areares);
// END FLOW ALGEBRA EXPRESSION EVALUATION
}
C++

## Slide 36: Maintaining to do Q and partition sharing
while(!finished) { //Loop within partition
while(!que.empty())
{ .... // FLOW ALGEBRA EXPRESSION EVALUATION
}
// Decrement neighbor dependence of downslope cell
flowData->getData(i, j, angle);
for(k=1; k<=8; k++) {
p = prop(angle, k);
if(p>0.0) {
in = i+d1[k]; jn = j+d2[k];
//Decrement the number of contributing neighbors in neighbor
neighbor->addToData(in,jn,(short)-1);
//Check if neighbor needs to be added to que
if(flowData->isInPartition(in,jn) && neighbor->getData(in, jn, tempShort) == 0 ){
temp.x=in; temp.y=jn;
que.push(temp);
}
}
}
}
//Pass information across partitions
areadinf->share();
neighbor->addBorders();
C++

## Slide 37: Python Script to Call Command Line
mpiexec –n 8 pitremove –z Logan.tif –fel Loganfel.tif

## Slide 38: PitRemove
Python

## Slide 39: Validation code to add default file names
Python

## Slide 40: Some TauDEM Demo’s
And fixing one of the functions …

## Slide 41: Conclusions
The GIS grid based terrain flow data model enables derivation of a wide variety of information useful for the study of hydrologic processes.
Terrain surface derivatives enhanced by use of DInfinity model.
Flow algebra a general “recipe” for terrain flow related modeling.
Parallelism required to process big terrain data.
Saw how to dip into GIS based programming