## Slide 1: Channel Identification in the Guadalupe Delta and Bayou System
Richard Carothers
11 November, 2014

## Slide 2: Study Area
Lower Guadalupe basin emptying into Mission Lake in SE TX in Calhoun, Refugio, Victoria counties.
1 m resolution Lidar dataset approximately 15 km by 25 km though the actual study area likely smaller
General Purpose
Identify water surfaces channels with an automated or semi-automated process

## Slide 3: Problem
Water hyacinth sits atop water and return signal as land
Water surface inhibits the reflection of laser waves providing “no return” or no elevation data
Normal Method

## Slide 4: NHD Dataset
Original NHD dataset provides features of water bodies, water “areas”, and flow lines
… But the dataset can be imprecise and even inaccurate

## Slide 5: Thresholding
Set elevation and/or slope thresholds to extract likely water surface locations.
This works well in some areas.
However, it works quite poorly in others.
Aquatic Vegetation
No Data
(water surface)
Aquatic Vegetation
No Data
(water surface)
Marsh
(land/aquatic veg)

## Slide 6
Other methods
TerEX toolbox
  Developed by Patrick Belmont et al at Utah State
  (http://www.cnr.usu.edu/htm/facstaff/belmont-hydrology-and-fine-sediment-lab/belmont-lab-resources)
Image Processing toolbox
  Provides a variety of filters to enhance feature contrast
Filter example taken from ESRI:
http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/Convolution_function/009t0000004s000000/

## Slide 7
Current Work
Bank identification by semi-automated cross section analysis
Develop custom flow lines based on NHD edits
Import into MATLAB and extract banks using feature of GeoNet2.0
Import bank locations back into GIS
Connect points to make polygons

## Slide 8
Problems
Cross sections work OK
Bank extraction works pretty well
Major problems with connections
Issue has to do with vector vs raster analysis

## Slide 9
Future Work
Either recode GeoNet2.0 or try HEC-RAS/GeoRas for bank extraction
Interpolate water surface elevations for area
Bathtub inundation model to establish connectivities