## Slide 1: Water Quality and Development in Hill Country
Jesse Libra
CE 394K

## Slide 2
Outline
Flying J Construction at Junction
Key Issue
Scope & Data
Methods
Analysis of Junction Site

## Slide 3
Flying J Junction Site

## Slide 4
Issues with the site:
In the Floodway/Floodplain
Drains towards the North Llano River via a TxDOT drainage ditch.

## Slide 5: *Southeastern Hill Country: Mason, Llano, Blanco, Kimble, Gillespie, Kerr, Kendall US Census Bureau
Chart: Southeastern Hill Country* population 2000 - 2050
| 36708 | 40269 | 40360 | 40725 | 41091 | 41456 | 54970
 | 156025 | 189039 | 189486 | 190879 | 192889 | 195675 | 309985
Project Justification
Problem
Population set to double by 2050
Counties have virtually no zoning power
Most small municipalities don’t have zoning ordinances
Goal
Identify areas where:
Major Highways (ADT > 5,000) intersect waterways within municipal limits
with:
  1) High runoff potential (High Curve Numbers)
  2) Overland flow to water body

## Slide 6: Counties: Mason, Llano, Kerr, and Kimble
Identifying Potential Sites:
TxDOT ADT data (2013)
Municipal boundaries
NDH Flow Lines
Runoff potential:
DEM30m
SSURGO USDA soil Data,
2006 National Land Cover data (2011 edition)
Overland Flow:
DEM 3m
Data

## Slide 7: Runoff Curve Numbers using HEC-GeoHMS
Approximates runoff potential
Land use + Slope + Soil Type
10 land use categories, 4 Soil Types
 | A | B | C | D
Pasture, grassland, or range | 39 | 61 | 74 | 78
Meadow | 30 | 58 | 71 | 78
Brush | 30 | 48 | 65 | 73
Forest | 30 | 55 | 70 | 77
Row Crops | 67 | 78 | 85 | 89

## Slide 8: Potential Maximum Soil Moisture
S0.20 = ((1000/CN) – 10))
S.05 = 1.33 x S0.201.15
Potential Maximum Soil Water Retention
Curve Number grid

## Slide 9
Characterization of Junction Site

## Slide 10
IH 10 ADT: 10,355
US 83 ADT: 5,458
Slope: 0.2 – 0.9 percent rise
Characterization of Junction Site

## Slide 11: Overland flow
Overland flow direction towards water body
Overland Flow

## Slide 12: Potential Maximum Soil Moisture
PMSWR 4.62 – 6.53 inches
Potential Maximum Soil Water Retention

## Slide 13: Current/Future work
Sites based on:
> 5000 ADT
Proximity to water body
Flow direction
Runoff potential during heavy rains
Within municipal boundaries
Current Work

## Slide 14: Questions?