## Slide 1: Arc Hydro Groundwater Data Model
GIS in Water Resources
Fall 2014
Some slides in this presentation are from Dr Norman Jones, Brigham Young University

## Slide 2: Resources
Hydro Resource Center: Groundwater http://resources.arcgis.com/en/communities/hydro/01vn00000011000000.htm
Groundwater Tools and Data Model http://www.aquaveo.com/archydro-groundwater
Tutorials http://www.aquaveo.com/ahgw-learning
Contact for tool support support@aquaveo.com

## Slide 3: Arc Hydro: GIS for Water Resources
Arc Hydro
  An ArcGIS data model for water resources
  Arc Hydro toolset for implementation
  Framework for linking hydrologic simulation models
The Arc Hydro data model and
application tools are in the public
domain
Published in 2002
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 4: Arc Hydro Groundwater: GIS For Hydrogeology
Describes the data model – public domain
Chapter for each data model component
Published in 2011
Notes: Notes:
Industrial partners: ESRI, Danish Hydraulic Institute, Camp,Dresser and McKee, Dodson and Associates
Government partners:
Federal: EPA, USGS, Corps of Engineers (Hydrologic Engineering Center)
State: Texas Natural Resource Conservation Commission, Texas Water Development Board
Local: Lower Colorado River Authority, City of Austin, Dept of Watershed Protection
Academic Partners: University of Texas, Brigham Young University, Utah State University

## Slide 5: Arc Hydro Groundwater Data Model
Notes: This is an overview diagram of the AHGW data model.
You can review the different components, talk about what each component is for:
Framework – includes hydrography, monitoring points, wells, aquifers, tables for managing time series (the framework includes a simplified temporal component). – with the framework you can get started on most water resources projects.
Borehole data – description of vertical information recorded along boreholes (hydrostratigraphy, well construction).
Geology – representation of data from geologic maps.
Hydrostratigraphy – building 2D and 3D hydrogeologic models including surfaces, cross sections, volumes.
Temporal – dealing with time varying data – plots, tracks, animations.
Simulation – integration with groundwater simulation models, especially MODFLOW.

## Slide 6: Arc Hydro Framework
Basic representation of surface water and groundwater
Components can be added to the framework to represent specific themes in more detail

## Slide 7: Aquifer features
Polygon features for representing aquifer boundaries

## Slide 8: Aquifer features
An aquifer is defined by one or a set of polygon features
Aquifer features can be grouped by HGUID

## Slide 9: Well
Location where the subsurface has been drilled
Attributes of wells describe the location, depth, water use, owner, etc.

## Slide 10: Well
Wells are defined as 2D point features
Only some basic attributes are predefined to describe the well use, and geometry and relationship with aquifers
Wells in the Edwards Aquifer

## Slide 11: Aquifer and well
Well features are related to Aquifers
An aquifer can be associated with one or more wells (1:M relationship)
Can take a different approach to support M:N relationship
*
HydroID
HydroCode
Name
HGUID
FType
Aquifer
HydroID
HydroCode
LandElev
WellDepth
AquiferID
AqCode
HGUID
FType
Well
1

## Slide 12: Aquifer and well
Well HydroID = 53

## Slide 13: Wells and TimeSeries
Well features are related with time series (water levels, water quality)
San Marcos springs
Springs
Sink Creek
San Marcos
Monitoring Well
(
295443097554201
)

## Slide 14: MonitoringPoint has time series
Monitoring points are related with time series (streamflow, water quality, precipitation)

## Slide 15: Integration of surface water and groundwater data
Streamflow Gage at Comal Springs, New Braunfels Texas
Well in the Edwards Aquifer)
The common framework supports analysis of surface water and groundwater data together

## Slide 16: Surface water - groundwater linkage
Relationships between surface water and aquifer enable analysis based on spatial and hydrologic relationships
Streams over the outcrop = recharge features

## Slide 17: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 18: Geologic maps
A geologic map is a cartographic product that portrays information about the geologic character of a specific geographic area
Groundwater features are closely tied to geology
Geologic maps vary in scale (continental, regional, local)
Provide a simple data structure to support mapping
Geology
Aquifers
Maps from the United States National Atlas (http://nationalatlas.gov/).

## Slide 19: Geology component
Map modified from: Geologic map of the Edwards Aquifer recharge zone, south-central Texas. U.S. Geological Survey SIM 2873
GeologyPoint: Point feature (e.g. springs, caves, sinks, and observation points)
GeologyLine: Line features (e.g. faults, contacts)
GeologyArea: Areal features (e.g. rock units and alteration zones)

## Slide 20: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 21: BoreholeLog table
Stores 3D borehole data related with well features
Each row represents a point/interval along a borehole
Data are related to Wells using the WellID attribute
3D geometry is defined by the TopElev and BottomElev attributes

## Slide 22: 3D features (BorePoints and BoreLines)
Can create 3D features representing data in the BoreholeLog table
BorePoint is a 3D point feature class for representing point locations along a borehole (e.g. geologic contacts, samples)
BoreLine is a 3D line feature class for representing intervals along a borehole

## Slide 23: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 24: Hydrogeologic units
“Hydrogeologic unit is any soil or rock unit or zone which by virtue of its hydraulic properties has a distinct influence on the storage or movement of ground water” (USGS glossary of hydrologic terms)
Hydrogeology can be derived by classifying stratigraphic units
Georgetown Fm. (GTOWN)
Cyclic + Marine member (CYMRN)
Upper confining unit
Leached + collapsed member (LCCLP)
Regional dense member (RGDNS)
Grainstone member (GRNSTN)
Kirschberg evaporite member (KSCH)
Dolomitic member (DOLO)
Upper Glen Rose (UGLRS)
Stratigraphic units
Hydrogeologic units
Pearson Fm.
Basal Nodular member (BSNOD)
Kainer Fm.
Georgetown Fm.
Edwards Aquifer

## Slide 25: Hydrogeologic unit table
HydroGeologicUnit table provides a conceptual description of hydrogeologic units
Hydrogeologic units can be attributed with an AquiferID such that they can be grouped to represent an aquifer
Spatial features are indexed with a HGUID to relate to the conceptual representation of the units

## Slide 26: Hydrogeologic unit table
Hydrogeologic units are described with different spatial instances (outcrops, borehole intervals, surfaces, cross sections, and volumes)
HGUID is the key attribute
HGUID
HGUID
Conceptual description
Spatial description
GeoArea
Polygon
feature class
HydrogeologicUnit
Table
SectionLine
PointZ
feature class
GeoRasters
Raster dataset
GeoSection
Multipatch
feature class
GeoVolume
Multipatch
feature class
1
*

## Slide 27: GeoArea
GeoArea feature representing the Kainer hydrogeologic unit
GeologyArea features represent data from geologic maps
GeologyArea
2D polygons defining boundaries of hydrogeologic units
GeoArea (conceptual/interpolated boundary) ≠ GeologyArea (mapped outcrop)
Data points representing top elevations of the Kainer formation

## Slide 28: Representation of Cross Sections
SectionLine defines the 2D cross section
GeoSection represent 3D sections as 3D features
SectionID of the polygon relates back to the section line
A
A’
B
B’

## Slide 29: GeoSections

## Slide 30: XS2D Component

## Slide 31: 2D Cross Section Editing
Outcrop
Salt water interface
Borehole data
Panel
Panel divider
Edit cross sections in ArcMap

## Slide 32: Transform to 3D GeoSection

## Slide 33: GeoRasters
Raster catalog for storing and indexing raster datasets
Can store top and bottom of formations
Each raster is related with a HGU in the hydrogeologic unit table
Georgetown
Glen Rose
Kainer
Person

## Slide 34: GeoRasters
GeoRasters also store hydraulic properties such as transmissivity, conductivity, and specific yield
K (feet/day)
Raster of hydraulic conductivity in the Edwards Aquifer

## Slide 35: GeoVolume
Objects for representing 3D volume objects
Geometry is multipatch - Can create the volumes as a set of 3D triangles
Not real volume – can’t do any 3D operations

## Slide 36: Components
Geology - Representation of data from geologic maps
Boreholes – Description of well attributes and borehole data
Hydrostratigraphy – 2D and 3D description of hydrostratigraphy
Temporal – Representation of time varying data
Simulation – Representation of groundwater simulation models (focus on MODFLOW)

## Slide 37: Space-time datasets

## Slide 38: Types of time varying datasets

## Slide 39: Variable Definition table
Catalog of time varying parameters (e.g. streamflow, water levels, concentrations, etc.)
Each variable is indexed with a HydroID

## Slide 40: TimeSeries table
Each measurement is indexed by space, time, and type
Space = FeatureID
Time = TsTime
Type = VarID
VarID provides information on the variable

## Slide 41: Time series views
We can “slice” through the data cube to get specific views of the data
Query by location
(FeatureID = 2791)
Where?
2791
TsTime
FeatureID
VarID
Query by type
(VarID = 6875)
What?
FeatureID
VarID
TsTime
6875
Query by location and type
(FeatureID = 2791 VarID = 6875)
Where and What?
2791
FeatureID
VarID
TsTime
6875

## Slide 42: Time series views
Well HydroID = 2791
Create a plot of time series related to a feature
Get all the data of VarID 6875 measured at Feature 2791

## Slide 43: Time series views
A type-time view: Get water levels (TSTypeID =2) for 1/1999
Water level in the Edwards Aquifer in 1/1999
Set of layers for different times creates an animation
1/1991
FeatureID
VarID
6875
TsTime

## Slide 44: Cloud-Based Water Level Mapping Utility
Norm Jones
Brigham Young University

## Slide 45: Component 2 Objective
Geodatabase
Model Files
GIS Workflow
Server
Web Mapping
Engineers, Decision Makers, Advocacy Groups, Public
Cloud-Based Modeling and Visualization

## Slide 46: Cloud-Based Water Level Mapping Utility
Detailed maps showing water level changes over time are essential for aquifer management and planning
Water
Level
Mapping
Utility
Inputs
Subregion
Date(s)
Outputs
Water Levels
Drawdown
Depth to GW
TWDB Well Database
Arc Hydro GW Tools
Python-Based Workflow
Google Earth Web Plug-in

## Slide 47: TWDB Well Database
274,904 wells w/meas.
781,864 measurements

## Slide 48: Measurements per Well

## Slide 49: Measurements per Year

## Slide 50: Wells
The Well location is defined as a 2D point in the Well feature class
In the Arc Hydro model we only predefine a set of basic attributes
Wells in the Edwards Aquifer

## Slide 51: Geoprocessing Tools

## Slide 52: Workflow Components
Query wells in selected region
Estimate water levels at selected date
Interpolate water levels to raster
Calculate Drawdown & Depth to GW
Export rasters to KMZ
Archives maps to database

## Slide 53: Time Series Interpolation
Water levels are measured sporadically
To get a value at each well, we must perform time series interpolation
time
Z

## Slide 54: Least Squares Fit
time
Z

## Slide 55: Least Squares Fit, n=2
time
Z

## Slide 56: Least Squares Fit, Extrapolation
time
Z

## Slide 57
Google Earth Plug-In
http://ci-water.groups.et.byu.net/groundwater1
For generating new maps
Archive of existing maps
Static map components

## Slide 58
Region Selection

## Slide 59
Water Level Map

## Slide 60
Depth to GW Map

## Slide 61
Depth to GW
Map

## Slide 62: Animations
12/25/1999
12/25/2000
12/25/2001
12/25/2002
12/25/2003
12/25/2004
12/25/2005

## Slide 63
Norm Jones
njones@byu.edu
http://www.ci-water.org
http://ci-water.groups.et.byu.net/groundwater1
Thank You!
This material is based upon work supported by the National Science Foundation under Grant
No. 1135482.
Special Thanks to:
Michael Burns
Scott Christiansen
Gil Strassberg

## Slide 64: Summary Concepts
Arc Hydro Groundwater…
  extends Arc Hydro to represent groundwater datasets in GIS
  includes components for aquifers, wells, hydrogeologic features, time series, and simulation model output
  links features to hydrogeologic layers via HGUID, and to aquifers via AquiferID