## Slide 1: Underground Representation and Imaging of Barnett Shale
Weili Lin
Environment and Water Resources Engineering
11/22/2016
Source: http://oilprice.com/Energy/Crude-Oil/Game-May-Not-Be-Over-For-Barnett-Shale.html
Notes: Joel

## Slide 2: Contents
Background
Objectives and Scope
Methods and Results
Outlook
Source: http://energy.gov/articles/producing-natural-gas-shale

## Slide 3
Background

## Slide 4
Source: Annual Energy Outlook 2016, EIA
Source: US Energy Information Administration http://www.eia.gov/oil_gas/rpd/shaleusa1_letter.pdf
Over 15,000 oil and gas wells drilled and hydraulic fractured in Barnett Shale by 2007.
Hydraulic fracturing uses chemicals that potentially contaminate water resource.
Barnett Shale gas play depth 6500 to 8000 feet.
Leak of hydraulic fracturing well casing will result in ground water contamination.

## Slide 5
Source:Vengosh, Avner, et al. "A critical review of the risks to water resources from unconventional shale gas development and hydraulic fracturing in the United States.
Over 15,000 oil and gas wells drilled and hydraulic fractured in Barnett Shale by 2007.
Hydraulic fracturing uses chemicals that potentially contaminate water resource.
Barnett Shale gas play depth 6500 to 8000 feet.
Leak of hydraulic fracturing well casing will result in ground water contamination.

## Slide 6: Objectives
Represent the underground formations, especially aquifers
Represent the wells in the Barnett Shale
ArcGIS Tools
Arc Hydro Groundwater (provided by Aquaveo and ESRI)
Hydrostratigraphy: Geosection
Source: http://www.archydrogw.com/Arc_Hydro_Groundwater_Data_Model.

## Slide 7: Geology of Barnett Shale
Land Surface Elevation
From Railroad Commission of Texas
Other Source may have different shape
Barnett Shale Outline
USGS NED30
Generally west – higher
east – lower
Maximum elevation 731 meter
Minimum elevation 71 meter

## Slide 8
Landcover
Barnett Shale Intersects with 46 counties
TexasCounty
Value | Classification | Area Percent (%)
21 | Developed, Open Space | 5.8243
41 | Deciduous Forest | 7.3300
42 | Evergreen Forest | 7.2187
52 | Shrub/Scrub | 22.8370
71 | Grassland/Herbaceous | 41.7871
82 | Cultivated Crops | 5.7391
 | Total Area | 69281.6769
National Land Cover Database 2011
*Low contribution not included

## Slide 9: Aquifers maps and Aquifer features
Polygon shape files from Texas Water Development Board (TWDB)
9 major aquifers (TX)
  3 intercept with Barnett
21 minor aquifers (TX)
  3 intercept with Barnett
Filled: Outcrop
Line-Shaded: Subcrop
Notes: The most basic features commonly used to represent groundwater systems are aquifers and wells. (page 23)
Artesian Aquifer - Aquifer in which ground water is confined under pressure that is significantly greater than atmospheric pressure. Synonym: Confined Aquifer. See also Unconfined Aquifer.
Aquifer - A geologic formation, group of formations, or part of a formation that contains sufficient saturated permeable material to yield significant quantities of water to springs and wells.
Ground water - In the broadest sense, all subsurface water; more commonly that part of the subsurface water in the saturated zone.

## Slide 10: Well Database and well features
TWDB: Texas Water Development Board
WellMain table contains spatial references.
Groundwater Database From TWDB
WellMain
StateWellNum
County
AquiferID
AqCode
LatitudeDD
LongitudeDD
LandElev
WellDepth
WellType
…
Notes: Wells are designed for many reasons: to produce water from aquifers, to monitor water levels and quality, and to inject (discharge) solutions into the subsurface.
WellType: Observation, Oil&Gas, Withdrawal of Water, WasteDisposal, etc.

## Slide 11: Well Database and well features
WellMain
StateWellNum
County
AquiferID
AqCode
LatitudeDD
LongitudeDD
LandElev
WellDepth
WellType
…
WaterQuality
StateWellNum
County
Aquifer
ParameterCode
…
WaterLevel
StateWellNum
County
DepthFromLSD
LandElevation
WaterElevation
…
WellBoreHole
StateWellNum
County
Aquifer
Diameter
TopDepth
BottomDepth
…
WellMain table serves as the central table, and is linked with additional tables describing all sorts of information.
Notes: Groundwater databases commonly have a central table that describes the location of wells and their properties. The central table is usually linked with additional tables describing information on the well construction, measurements of water levels and water quality taken at the wells, and descriptions of the formation material observed along boreholes.

## Slide 12: Well Database and well features
WellBoreHole
StateWellNum
County
Aquifer
Diameter
TopDepth
BottomDepth
…
AbsElev
550
540
520
490
Depth
Depth
0
10
30
0
10
50
530
WellMain
StateWellNum
County
AquiferID
AqCode
LatitudeDD
LongitudeDD
LandElev
WellDepth
WellType
…
Drilling Logs
Eg. Strata Observed
BoreholeLog
StateWellNumber
RefElev
FromDepth
ToDepth
TopElev
BottomElev
…
Notes: In the previous slide we represent each wellpoint as a point in a 2-D graph, but actually each well is a 3-D object, including the depth of the well. And most of the underground data is actually data from the wells we drill.
Material Text Description of strata observed along a borehole. Usually documented in drilling logs and later classified into geologic/hydrogeologic units.

## Slide 13: Arc Hydro framework
Unique Identifiers:
  Aquifer: HydroID
  Well: HydroID
The obtainment of BoreholeLog table and the subsequent boreline building can be carried out by Arc Hydro Groundwater Tools.
Source: http://www.archydrogw.com/images/c/c2/Archydrogw_wellsandboreholes.JPG

## Slide 14: Arc Hydro Groundwater Overview
http://www.aquaveo.com/software/ahgw-archydro-groundwater-introduction

## Slide 15: Project Objectives
http://www.archydrogw.com/images/9/9c/Archydrogw_overview.JPG

## Slide 16: Arc Hydro Groundwater - Oohs

## Slide 17: Challenges and Outlook
Challenges:
  Software requirements.
  Scarcity of well data.
Outlook:
  Borelines Building
  Hydrostratigraphy Construction
  3D Representation of Cross Sections

## Slide 18
Acknowledgements:
Weili Lin
11/22/2016
Dr. David Maidment
Dr. Timothy Whiteaker
Thank you!