## Slide 1: Evaluation of a Novel Method for Estimating Directly Connected Impervious Area and Unconnected Impervious Area
Andrew Chu, with help from Jones Edmunds and Associates
11/13/2018
University of Texas at Austin- CE 394k

## Slide 2: Example of Directly Connected Impervious Area (DCIA)
Directly Connected Impervious Area – Rain that falls on this area flows directly to the drainage system over impervious area.
Source: (Timbdesign, 1)

## Slide 3: Example of Unconnected Impervious Area (UCIA)
Unconnected impervious area- Rain that falls in this area must flow over a pervious area before it enters the drainage system.
Source: (Timbdesign, 1)

## Slide 5: Curve Number Reduction based on DCIA Percentage
Source: (United States, 1)

## Slide 6: 3 Methods for determining DCIA
Manual Scanning
The Gregory Method
Representative Sampling

## Slide 7: Example of Manual Scanning

## Slide 8: Performing the Gregory method
For each grid cell:
Calculate the unweighted Flow Length downstream
Calculate the Flow Length downstream weighted by impervious area.
  The impervious raster has values of 0 for pervious area and 1 for impervious area.
DCIA index =
Grid cells with values close to 1 are likely to be Directly Connected Impervious Area.
All values above a threshold DCIA index are considered Directly Connected Impervious Area.

## Slide 9: Physical Interpretation of the output- The DCIA index.
1 = impervious
0 = pervious

## Slide 11
Chart: 
| 0.95 | 0.9 | 0.85 | 0.8 | 0.75
Impervious Area vs. DCIA Index Cutoff | 2.7713 | 3.764 | 4.6441 | 5.6801 | 9.3765

## Slide 12: Comparison of DCIA estimation Methods
Comparison of DCIA Estimation Methods |  |  | 
Estimation Method | DCIA | Error | Time to completion
 | (ft^2) | (%) | (hours)
Gregory Method (0.95) | 2771306 | 69% | 1.25
Gregory Method (0.90) | 3763988 | 58% | 
Gregory Method (0.85) | 4644062 | 48% | 
Gregory Method (0.80) | 5680088 | 37% | 
Gregory Method (0.75) | 9376512 | 4% | 
Manual Method | 9008680 | 0% | 27
Land Cover Estimate Method | TBD | TBD | TBD

## Slide 13: Strengths of the Gregory Method
Strengths
  Fast
  Detailed- The Gregory method can analyze every grid cell
  Consistent
  Does not require human work.
  The output is probabilistic, not binary

## Slide 14: Weaknesses of the Gregory Method
Weaknesses
  Uncalibrated Accuracy Issues
  Fundamental
    Method requires a flow direction raster
    Sometimes pervious area gets classified as DCIA
    DCIA estimates for areas near the point of concentration are less accurate
    Requires calibration
    Uses D8 flow directions- May not represent reality at the 2.5ft grid cell level
    The end of the flow lines are not necessarily at the beginning of the stormwater system

## Slide 15: Improvements to the Gregory Method
Restrict DCIA index calculation to only impervious areas
Restrict Flow Length
Develop a method for consistently calibration of the Gregory Method
Use Dinfinity flow directions

## Slide 16: Works Cited
  Timbdesign. “Asphalt Driveways Minnesota | Residential Paving.” Alpine Asphalt, Alpine Asphalt, 9 Nov. 2018, alpineasphalt.com/residential/.
  United States, Congress, “Urban Hydrology for Small Watersheds.” Urban Hydrology for Small Watersheds, pp. 1–164.