## Slide 1: Spatial Analysis Using Grids
By the end of this class you should be able to:
describe some ways continuous surfaces or spatial fields are represented in GIS
list and describe the data elements that comprise a grid data structure
describe how integer, categorical and real valued data fields are represented using grids
use map algebra to perform raster calculations on grids and explain the scale issues involved in raster calculations where grids may not have the same cell size
define interpolation and describe aspects to be considered in interpolating a spatial field
use interpolation to determine watershed average precipitation (Ex 3)
calculate the slope of a topographic surface represented by a grid using:
  ArcGIS method based on finite differences,
  D8 model in direction of steepest single flow direction,
  D model in direction of steepest outward slope on grid centered triangular facets.
Learning Objectives

## Slide 2: Readings - Theory
ArcMap help: What is raster data? http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/what-is-raster-data.htm
ArcMap help: Fundamentals of raster data from Cell size of raster data to Raster dataset attribute tables http://desktop.arcgis.com/en/arcmap/latest/manage-data/raster-and-images/cell-size-of-raster-data.htm

## Slide 3
ArcGIS Pro An overview of the Spatial Analyst Toolbox https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/an-overview-of-the-spatial-analyst-toolbox.htm.
Readings – ArcGIS Pro Tools
Read this to get a general sense of the tools available. Tools we will use now or later include, from the Surface toolset: Slope, Aspect, Contour; from the Zonal toolset: Zonal Statistics; from Map Algebra: Raster Calculator; from Interpolation: Spline and Kriging; and many tools in the Hydrology toolset.

## Slide 4: Readings – Slope and Aspect
How Slope Works https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/how-slope-works.htm
How Aspect Works https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/how-aspect-works.htm

## Slide 5: Slope Handout
Determine the length, slope and azimuth of the line AB.
http://hydrology.usu.edu/dtarb/giswr/2017/Slope.pdf

## Slide 6: Two fundamental ways of representing geography are discrete objects and fields.
x
y
f(x,y)
The discrete object view represents the real world as objects with well defined boundaries in empty space.
The field view represents the real world as a finite number of variables, each one defined at each possible position.
(x1,y1)
Points
Lines
Polygons
Continuous surface
Features (Shapefiles)
Rasters
Notes: DRM

## Slide 7: Numerical representation of a spatial surface (field)
Grid or Raster
TIN
Contour and flowline

## Slide 8: Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells
Notes: DRM

## Slide 9: Line as a Sequence of Cells

## Slide 10: Polygon as Zone of Grid Cells
From: http://resources.arcgis.com/en/help/main/10.2/index.html#/How_features_are_represented_in_a_raster/009t00000006000000/

## Slide 11: Raster and Vector are two methods of representing geographic data in GIS
Both represent different ways to encode and generalize geographic phenomena
Both can be used to code both fields and discrete objects
In practice a strong association between raster and fields and vector and discrete objects
Notes: DRM

## Slide 12: A grid defines geographic space as a mesh of identically-sized square cells. Each cell holds a numeric value that measures a geographic attribute (like elevation) for that unit of space.

## Slide 13: The grid data structure
Grid size is defined by extent, spacing and no data value information
  Number of rows, number of column
  Cell sizes (X and Y)
  Top, left , bottom and right coordinates
Grid values
  Real (floating decimal point)
  Integer (may have associated attribute table)
Number
of
rows
Number of Columns
(X,Y)
Cell size
NODATA cell

## Slide 14: NODATA Cells

## Slide 15: Cell Networks

## Slide 16: Floating Point Grids
Continuous data surfaces using floating point or decimal numbers

## Slide 17: Integer valued grids to represent zones

## Slide 18: Value attribute table for categorical (integer) grid data
Attributes of grid zones

## Slide 19: Raster Sampling
from Michael F. Goodchild. (1997) Rasters, NCGIA Core Curriculum in GIScience, http://www.ncgia.ucsb.edu/giscc/units/u055/u055.html, posted October 23, 1997

## Slide 20: Cell size of raster data
From http://help.arcgis.com/en/arcgisdesktop/10.0/help/index.html#/Cell_size_of_raster_data/009t00000004000000/

## Slide 21: Raster Generalization
Central point rule
Largest share rule

## Slide 22: Map Algebra/Raster Calculation
Precipitation
-
Losses (Evaporation, Infiltration)
=
Runoff
5
2
2
3
2
4
3
3
7
6
5
6
-
=
Cell by cell evaluation of mathematical functions
Example

## Slide 23: Cell based discharge mapping by accumulation of generated runoff
Radar Precipitation grid
Soil and land use grid
Runoff grid from raster calculator operations implementing runoff generation formula’s
Accumulation of runoff within watersheds

## Slide 24: Raster calculation – some subtleties
Analysis extent
+
=
Analysis cell size
Analysis mask
Resampling or interpolation (and reprojection) of inputs to target extent, cell size, and projection within region defined by analysis mask

## Slide 25
4
3.1
4
6
150 m
150 m
2.2
3
4
3.5
2.5
2.7
2
1.5
1.8
100 m
100 m
Runoff R = P-f
Runoff Generation Raster Calculation Example
Precipitation, P cm/hr
Infiltration Rate, f cm/hr

## Slide 26: Lets Experiment with this in ArcGIS
precip.asc
ncols 2
nrows 2
xllcorner 0
yllcorner 0
cellsize 150
NODATA_value -9999
4 6
3.1 4
infiltration.asc
ncols 3
nrows 3
xllcorner 0
yllcorner 0
cellsize 100
NODATA_value -9999
2.2 3 4
1.8 2.5 3.5
1.5 2 2.7

## Slide 27: Runoff calculation using Raster Calculator
“precip.asc” - “infiltration.asc”

## Slide 28: The Result
1.8
2
1.6
1.3
Outputs are on 150 m grid.
How were values obtained ?

## Slide 29: Nearest Neighbor Resampling with Cellsize Maximum of Inputs
100 m
2.2
3
4
3.5
2.5
2.7
2
1.5
1.8
4
3.1
4
6
150 m
4 - 2.2 = 1.8
6 - 4 = 2
1.8
2
1.6
1.3
3.1 – 1.5 = 1.6
4 – 2.7= 1.3

## Slide 30: Inferences
ArcGIS has used nearest neighbors to align cells
ArcGIS has done raster computation at the scale of the coarsest input
  Is this what we want?
  How to control scale?
  What is meant by scale in this context?

## Slide 31: The scale triplet
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.
a) Extent
b) Spacing
c) Support

## Slide 32: Scale and the interpretation of data
From: Blöschl, G., (1996), Scale and Scaling in Hydrology, Habilitationsschrift, Weiner Mitteilungen Wasser Abwasser Gewasser, Wien, 346 p.

## Slide 33: Resample to get consistent cell size
4
6
3.1
4
5
3.55
3.55
5
4.275
4
6
3.1
4
Spacing & Support
Method

## Slide 34: Calculation with consistent 100 m cell size grid
Outputs are on 100 m grid as desired.
How were values obtained ?
“precip100” - “infiltration”
1.8
2
2
1.75
1.775
1.5
1.6
1.55
1.3

## Slide 35: 100 m cell size raster calculation
100 m
4 – 2.2 = 1.8
3.55 – 1.8 = 1.75
5 – 3.5 = 1.5
4 – 2.7 = 1.3
5 – 3 = 2
6 – 4 = 2
4.275 – 2.5 = 1.775
3.1 – 1.5 = 1.6
3.55 – 2 = 1.55
1.8
2
2
1.75
1.775
1.5
1.6
1.55
1.3
100 m
4
3.1
4
5
3.55
3.55
5
4.275
6
2.2
3
4
3.5
2.5
2.7
2
1.5
1.8

## Slide 36: Interpolation
Nearest neighbor
Inverse distance weight
Bilinear interpolation
Kriging (best linear unbiased estimator)
Spline
Estimate values between known values.
A set of spatial analyst functions that predict values for a surface from a limited number of sample points creating a continuous raster.

## Slide 37: Interpolation Comparison
Grayson, R. and G. Blöschl, ed. (2000)

## Slide 38: Further Reading
Grayson, R. and G. Blöschl, ed. (2000), Spatial Patterns in Catchment Hydrology: Observations and Modelling, Cambridge University Press, Cambridge, 432 p.
Chapter 2. Spatial Observations and Interpolation
http://www.hydro.tuwien.ac.at/forschung/publikationen/engl-publikationen/spatial-patterns-in-catchment-hydrology.html
Full text online at:

## Slide 39
3-D detail of the Tongue river at the WY/Mont border from LIDAR.
Roberto Gutierrez University of Texas at Austin
Analysis of topographic surfaces represented by a Digital Elevation Model (DEM)

## Slide 40: Topographic Slope
Defined or represented by one of the following
  Surface derivative z. Given z(x,y) evaluate (dz/dx, dz/dy)
  Vector with x and y components (Sx, Sy)
  Vector with magnitude (slope) and direction (aspect) (S, )
See http://hydrology.usu.edu/dtarb/giswr/2018/Slope.pdf

## Slide 41: Slope and Aspect
= aspect clockwise from North
https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/how-slope-works.htm

## Slide 42
g
d
a
h
e
b
i
f
c
Similarly
Slope magnitude =
ArcGIS “Slope” tool
a
b
c
d
e
f
g
h
i
x
y
x
y

## Slide 43: ArcGIS Aspect – the steepest downslope direction
Use atan2 to resolve ambiguity in atan direction
https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/how-aspect-works.htm

## Slide 44
Example
30
80
74
63
69
67
56
60
52
48
a
b
c
d
e
f
g
h
i
145.2o

## Slide 45
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope (Flow Direction Tool)
- Direction of Steepest Descent
30

## Slide 46
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
ESRI Direction encoding

## Slide 47: Limitation due to 8 grid directions.
?

## Slide 48
The D Algorithm
Tarboton, D. G., (1997), "A New Method for the Determination of Flow Directions and Contributing Areas in Grid Digital Elevation Models," Water Resources Research, 33(2): 309-319.) (http://www.engineering.usu.edu/cee/faculty/dtarb/dinf.pdf)

## Slide 49
The D Algorithm
If 1 does not fit within the triangle the angle is chosen along the steepest edge or diagonal resulting in a slope and direction equivalent to D8

Elevations at each vertex zi
z2
z1
z0

## Slide 50
D∞ Example
30
eo
e7
e8
14.9o
284.9o
80
74
63
69
67
56
60
52
48
From ArcGIS Pro Help:

## Slide 51: Summary Concepts
Grid (raster) data structures represent surfaces as an array of grid cells
Raster calculation involves algebraic like operations on grids
Interpolation and Generalization is an inherent part of the raster data representation

## Slide 52: Summary Concepts (2)
The elevation surface represented by a grid digital elevation model is used to derive slope important for surface flow
The eight direction pour point model approximates the surface flow using eight discrete grid directions.
The D vector surface flow model approximates the surface flow as a flow vector from each grid cell apportioned between down slope grid cells.